## Slide 1: Chapter 6: Introduction to Caching
Chapter 6 Topics:
  The concept of a cache
  Locality of reference
  Stride-1 vs Stride-N referencing
  Cache hit/miss rates
  Cache-friendly code

## Slide 2: Announcements
Recitation exercise due this Friday before midnight
Performance Lab #4 due Mon November 13
  Optimize code to improve performance
Midterm #3 Wednesday Nov 15
  Same procedure as before, except sections 101-103 go to EKLC 1B20 (Ekeley Sciences near Norlin) – room only fits about 3 recitation sections, not 4 (we were not able to get the Hellems room)
  Topics: Chapters 4-6 on optimization techniques
Read:
  Chapter 6, and do practice problems

## Slide 3: Chapter Mapping
Lines of
Source
code
Lines of
Assembly
code
Lines of
Binary
code &
data
10101010
00001010
01010111
Memory
11101110
00111011
10000111
10101010
add a,b
sub a,b
move a…
Chapter 3
Chapters 3, 4, 5 and 6
Chapter 7
Chapter 9
Chapter 5
Chapter 2
Pre-processor
&
Compiler
Assembler
&
Linker
Operating
System
Chapter 8

## Slide 4: Typical Computer Organization Connecting CPU and Memory
CPU and main memory are connected by a communication bus.
A bus is a collection of parallel wires that carry address, data, and control signals.
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus
Notes: Front-side buses between Intel CPUs and main memory typically run at around 100 MHz * 4 transfers/cycle * 8 bytes wide = 3.2 GB/sec

## Slide 5: Memory Read Transaction
Main memory reads address for A from the memory bus, retrieves word x (A’s value), and places it on the bus.
ALU
register file
bus interface
x
0
A
x
main memory
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 6: Memory Write Transaction
CPU places data word y on the bus and address of A to store A’s value in memory location for A.
y
ALU
register file
bus interface
y
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 7: Random-Access Memory (RAM)
Key features
  RAM is packaged as a chip.
  Basic storage unit is a cell (one bit per cell).
  Multiple RAM chips form a memory.
  Volatile storage – loss of power causes loss of stored bits
Static RAM (SRAM)
  Each cell stores bit with a six-transistor circuit.
  Retains value indefinitely, as long as it is kept powered.
  Relatively insensitive to disturbances such as electrical noise.
  Faster and more expensive than DRAM.
Dynamic RAM (DRAM)
  Each cell stores bit with a capacitor and transistor.
  Value must be refreshed every 10-100 ms.
  Sensitive to disturbances.
  Slower and cheaper than SRAM.

## Slide 8: SRAM vs DRAM Summary
Tran. Access
per bit time Persist? Sensitive? Cost Applications
SRAM 6 1X Yes No 100x cache memories
DRAM 1 10X No Yes 1X Main memories,
frame buffers

## Slide 9: The CPU-Memory Gap
The increasing gap between DRAM, disk, and CPU speeds.
DRAM is inexpensive but slow, SRAM is 100X more expensive but 10X faster
So use DRAM for main memory, and SRAM for smaller caches in CPU

## Slide 10: Adding Caching Memory to CPU
  Store commonly accessed data and instructions in CPU caches
  These caches have faster access times, higher throughput, but cost more, so can’t be as large as main memory
  Benefit: Faster average access times, but only if the access patterns for data and instructions exhibit enough locality
  Want a high cache hit rate, and a low cache miss rate

## Slide 11: Locality
Principle of Locality:
  Programs tend to reuse data and instructions near those they have used recently, or that were recently referenced themselves.
  Temporal locality: Recently referenced items are likely to be referenced in the near future.
    e.g. instructions in a loop, or data variables referenced in a loop
  Spatial locality: Items with nearby addresses tend to be referenced close together in time.
    e.g. array elements a[i] and a[i+1] tend to be referenced in sequence, or instructions like “pop %epb” and “ret” tend to be referenced in sequence

## Slide 12: Locality Example
Data:
  Temporal: sum referenced in each iteration
  Spatial: array a[] accessed in memory in succession, i.e. via a stride-1 pattern (sequential in row-major order)
Instructions:
  Temporal: cycle through loop repeatedly
  Spatial: reference instructions in memory in sequence, looping repeatedly
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;

## Slide 13: Layout of Arrays in Memory (review)
Arrays allocated sequentially
  each following element is in a higher contiguous memory location
  e.g. if a[] is an int array, then a[i+1] is located 4 bytes higher than a[i], etc.
Accessing the array sequentially in the same order it is allocated
  for (i = 0; i < N; i++)
    sum += a[i];
  accesses successive elements in memory, column by column
  Stride-1 access pattern
a[0]
a[1]
a[2]
a[3]
High
Low
Main
Memory
Notes: This is true of C arrays.

## Slide 14: Layout of Arrays in Memory (review)
Multi-dimensional arrays allocated sequentially in row-major order
  Lay out the first row first, then the second row next, followed by the third row, etc.
  Within each row, lay out each subsequent element (column) in a higher contiguous memory location
  e.g. if a[][] is a 2-D int array, then
    a[i][j+1] is located 4 bytes higher than a[i][j]
    a[i+1][j] is located 4*N bytes higher than a[i][j], where N=# columns
a[0][0]
a[0][1]
a[0][2]
a[0][3]
a[1][0]
a[1][1]
a[1][2]
a[1][3]
a[2][0]
a[2][1]
a[2][2]
a[2][3]
High
Low
Main
Memory
row 0
row 1
row 2
Notes: This is true of C arrays.

## Slide 15: Locality Example (2)
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
This function reads a[] in row-major order, as it is laid out in memory, and has good spatial locality
  Inner loop reads elements of 1st row in order, then 2nd, etc.
  Stride-1 reference pattern
int sumarrayrows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum
}

## Slide 16: Locality Example (3)
Scans the array column-wise instead of row-wise
  Does this change the value of the sum?
    No
  This exhibits a Stride-N reference pattern: a[0][j], then a[1][j], then a[2][j] – each successive memory location in the inner loop is N int’s apart
    This function exhibits poor spatial locality - can’t take advantage of the fact that data is fetched as a block of contiguous nearby data words and then is cached
int sumarraycols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum
}

## Slide 17: Stride-N Reference Pattern
a Stride-N access pattern jumps from row to row, incrementing by N elements or columns each jump
a[0][0]
a[0][1]
a[0][2]
a[0][3]
a[1][0]
a[1][1]
a[1][2]
a[1][3]
a[2][0]
a[2][1]
a[2][2]
a[2][3]
High
Low
Main
Memory
row 0
row 1
row 2
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
N
elements

## Slide 18: Locality Example (4)
Question: Can you permute the loops so that the function scans the 3-d array a[] with a stride-1 reference pattern (and thus has good spatial locality)?
int sumarray3d(int a[N][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < N; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum
}
Answer: k on outside loop, i on middle loop, j on inner loop
Notes: This is Stride-N^2!
Permuting the loop indices to obtain Stride-1 access is essential to optimizing the performance of your perf lab.

## Slide 19: Stride-1, Caching & Spatial Locality
Stride-1:
  for (j = 0; j < N; j++)
    sum += a[0][j];
  accesses successive elements in memory
  1st access to a[0][0] pulls in a cache block B worth of bytes containing a[0][0]
  If cache block size B > size of each word W in array a, then exploit spatial locality
    i.e. cache block B contains not just a[0][0], but a[0][1], a[0][2], …
  Example: if ‘a’ is an int array, and B stores 4 int’s per cache block (i.e. B=16 bytes), then
    accessing a[0][0] will cause a cache miss, pulling in a[0][0], a[0][1], a[0][2] and a[0][3] from memory
    When a[0][1], a[0][2] and a[0][3] are next accessed sequentially by the loop, they’re already in cache!
    So for every four accesses to the array a[i][j], we get 1 miss and 3 hits, for a miss rate of ¼=25%

## Slide 20: Writing Cache Friendly Code
Repeated references to variables are good (temporal locality)
Stride-1 reference patterns are good (spatial locality)
Examples:
  cold cache, 4-byte words, 4-word cache blocks
int sumarrayrows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
Miss rate =
1/4 = 25%
a[0][0] causes a cache miss, which brings in 4 words a[0][0] – a[0][3]
a[0][1] is a cache hit, as is a[0][2] and a[0][3]
a[0][4] causes a cache miss, bring in a[0][4]-a[0][7]
Cache hits on a[0][5]-a[0][7]
Etc…

## Slide 21: Stride-N, Caching & Spatial Locality
Stepping through rows in one column: (Stride-N)
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    When a[0][0] is accessed, there’s a miss, so pull in a[0][0], a[0][1], a[0][2], a[0][3].
    Next a[1][0] is accessed but it’s not in the cache! So a miss. Fetch a[1][0], a[1][1], a[1][2], and a[1][3].
    Next a[2][0] is accessed, but it’s not in the cache!
    Each access a[0][0], a[1][0], a[2][0], … causes a cache miss
    So the miss rate = 1 (i.e. 100%)
  So penalty for a Stride-N access pattern is huge – may have to go to memory every time, suffering a large latency hit (~100X)

## Slide 22: Writing Cache Friendly Code (2)
Repeated references to variables are good (temporal locality)
Stride-N reference patterns are bad (poor spatial locality)
Examples:
  cold cache, 4-byte words, 4-word cache blocks
int sumarraycols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Miss rate =
100%
a[0][0] causes a cache miss, which brings in 4 words a[0][0] – a[0][3]
a[1][0] is a cache miss, brings in a[1][0] – a[1][3]
a[2][0] is a cache miss, brings in a[2][0] – a[2][3]
Etc…

## Slide 23: Matrix Multiplication Example
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i][j] += a[i][k] * b[k][j];
}
Description:
  Multiply two N x N matrices
  O(N3) total operations
    Typically 3 loops
  Accesses
    N reads per source element
    N values summed per destination
      but may be able to hold in register

## Slide 24: Matrix Multiplication Example (2)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register
Major Cache Effects to Consider
  Total cache size
    Exploit temporal locality and keep the working set small (e.g., by using blocking)
  Block size
    Exploit spatial locality

## Slide 25: Matrix Multiplication Example (2)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Analysis Method:
  Look at access pattern of inner loop
C
A
k
i
B
k
j
i
j
Assume in the following analysis:
  Line size = 32B (big enough for 4 64-bit words)
  Matrix dimension (N) is very large
  Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows

## Slide 26: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.25 1.0 0.0

## Slide 27: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.25 1.0 0.0

## Slide 28: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.0 0.25 0.25

## Slide 29: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.0 0.25 0.25

## Slide 30: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column -
wise
Column-
wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  1.0 0.0 1.0

## Slide 31: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per Inner Loop Iteration:
  A B C
  1.0 0.0 1.0

## Slide 32: Summary of Matrix Multiplication
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.25
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.5
  Stride-1 for both
  inner arrays
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0
  Stride-N for both
  inner arrays
Cache-Friendly
Code!

## Slide 33: Core i7 Matrix Multiply Performance
Actual inner loop performance = f(miss rate, # loads & stores)
1.25 misses
0.5 misses/Stride-1
2.0 misses/Stride-N
Notes: Why does # cycles vary with array size? For small arrays, most of array can fit into L1 cache. See memory mountain analysis.

## Slide 34: Chapters 6: Cache Indexing
Topics:
  Types of caches:
    Direct-mapped,
    Set Associative,
    Fully Associative

## Slide 35: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 36: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)
Notes: A typical cache replacement policy is least recently used (LRU)

## Slide 37: Caching in a Memory Hierarchy
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Larger, slower, cheaper storage
device at level k+1 is partitioned
into blocks.
Data is copied between
levels in block-sized transfer units
8
9
14
3
Smaller, faster, more expensive
device at level k caches a
subset of the blocks from level k+1
Level k:
Level k+1:
4
4
4
10
10
10

## Slide 38: General Caching Concepts
Request
14
Request
12
Program needs object d, which is stored in some block b.
Cache hit
  Program finds b in the cache at level k. E.g., block 14.
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
14
12
14
4*
4*
12
12
0
1
2
3
Request
12
4*
4*
12
Cache miss
  b is not at level k, so level k cache must fetch it from level k+1. E.g., block 12.
  If level k cache is full, then some current block must be replaced (evicted). Which one is the “victim”?
    Placement policy: where can the new block go? E.g., b mod 4
    Replacement policy: which block should be evicted? E.g., LRU

## Slide 39: Types of Cache Misses
Cold (compulsory) miss
  Occurs on first access to a block
  Need to “warm up” cache in the beginning
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache
Conflict miss
  Most hardware caches limit blocks to a small subset (sometimes a singleton) of the available cache slots
    e.g., block i must be placed in slot (i mod 4)
  Conflict misses occur when the cache is large enough, but multiple data objects all map to the same slot
    e.g., referencing blocks 0, 8, 0, 8, ... would miss every time if placement policy is (i mod 4) and there is only one slot

## Slide 40: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    1-2 clock cycle for L1
    5-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 41: Average Cache Performance
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 0.97 * 1 cycle + 0.03 * 100 cycles ≈ 4 cycles
  99% hits: 0.99 * 1 cycle + 0.01 * 100 cycles ≈ 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 42: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
For L1 hardware caches, access must be fast, so organize as follows:
Cache size:
S x E x B data bytes
Cache organized this
way for fast access
Notes: Cache is organized this way for fast access. Cache can look at a memory address, and quickly determine its row. Within the row, parallel digital logic will compare the memory address to each tag using essentially an AND (and also with the valid bit), and if the AND is true for a particular line, then that line’s data will be output (in particular, the byte offset into that line will be offset). This parallel comparison to each tag in the row is fast and the whole row and column comparison takes 2-3 cycles.

## Slide 43: Cache Access Example
E = 8 lines per set
S =
4 sets
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
  Suppose cache stores 32-bit data or instructions = 4 bytes/block or line
  Each cached block is taken from a location in memory, so could use the cached block’s full memory address as its identifier or tag.
  But since each block is 4 bytes long, then the memory addresses of blocks are unique only to a factor of 4
  Lower 2 bits of address not needed in tagging a block. (b=2)

## Slide 44: Cache Access Example (2)
E = 8 lines per set
S =
4 sets
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
  Of remaining 30 bits, suppose the hash function separates these into 4 sets: the set or row that an address belongs to in the cache = hash h(top 30 bits of address) = (top 30 bits of address) mod 4
    This hashes an address into 1 of 4 hash buckets/rows or sets, as shown above.
  Thus, the next 2 lower order bits are used to identify a row (s=2)
Within a row, tag size t = 32 - (2+2) = 28 bits
  Tag of cache block = top 28 bits (t=28)
  Match these tags with the input address

## Slide 45: Why Use Middle Bits as Index/Hash?
High-Order Bit Indexing
  Adjacent memory lines would map to same cache entry
  Poor use of spatial locality
4-set Cache
00
01
10
11
High-Order
Bit Indexing
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Middle-Order
Bit Indexing
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Middle-Order Bit Indexing
  Consecutive memory lines map to different cache lines
  Can hold C-byte region of address space in cache at one time
t bits
s bits
b bits
t bits
s bits
b bits
Notes: In general, if there is more than one column, unlike this case, adjacent memory lines would map to the same cache row. Eventually, the cache would run out of space on the row and start evicting entries on the row. If the program needs to access those elements again, via temporal locality, then there’s be many cache misses. Instead, by using middle order bit indexing, the cache spreads out (more* data that is accessed recently, using the whole space of the cache to store in this case 4X more recently used data than the high order bit indexing approach.

## Slide 46: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 47: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 48: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag

## Slide 49: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
If no match: old line is evicted and replaced
int (4 Bytes) is here

## Slide 50: Direct-Mapped Cache Simulation
M=16 bytes of addresses, B=2 bytes/block,
S=4 sets, E=1 entry/set
x
t=1
s=2
b=1
xx
x
1
0
m[1] m[0]
v
tag
data
0 [00002] (miss)
(1)
13 [11012] (miss)
8 [10002] (miss)
0 [00002] (miss)
0
M[0-1]
1
1
1
m[9] m[8]
v
tag
data
(4)
1
M[12-13]
1
1
M[8-9]
1
1
0
m[1] m[0]
v
tag
data
1
1
m[13] m[12]
(5)
1
M[12-13]
1
0
M[0-1]
1
1
0
m[1] m[0]
v
tag
data
1
1
m[13] m[12]
(3)
1
M[12-13]
1
0
M[0-1]
1
(2)
hit
Address trace (reads):
0 [00002], 1 [00012], 13 [11012], 8 [10002], 0 [00002]

## Slide 51: Direct-Mapped Cache Performance Problem
float dotprod(float x[8], float y[8])
{
int i;
float sum = 0;
for (i = 0; i < 8; i++)
sum += x[i]*y[i];
return sum;
}
One block = 16 bytes = 4 floats
Assume x[] is loaded into 32 bytes of contiguous memory at address A divisible by 32, and y[] starts immediately after x[]
Each x[i] and y[i] maps to the identical cache set
On first iteration, x[0] is a cache miss, so pull in x[0]-x[3].
Next, need y[0], also a cache miss, so pull in y[0]-y[3] – replaces x[0]-x[3]!
x[1] misses, overwriting y[0]-y[3], etc…, so we get thrashing
Set 0
Set 1

## Slide 52: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
Higher associativity E reduces amount of thrashing
But note: if your data access pattern maps to the same row of a cache,
and rotates through 2*E data items, then you’ll still get thrashing

## Slide 53: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag

## Slide 54: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
match both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
If no match and full (both lines valid):
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 55: Fully Associative Caches
Consists of a single set, i.e. S=1, and C = E*B, or E=C/B
  All the work is done in line matching and word selection
  This works the same as for earlier caches
  This is expensive, requiring more parallel circuitry for matching
  This is reserved for special caches, e.g. TLBs
E = 2e lines per set
S =
1 set
B = 2b bytes per cache block (the data)

## Slide 56: What about writes?
Multiple copies of data exist:
  L1, L2, L3, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes immediately to memory)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate
Notes: Write-allocate brings in a block of memory, and the hope is that the next write will be Stride-1 to the next word in the now-cached block of memory.
Write-through updates each level of hierarchy, and hence incurs a lot of bus traffic. Write-back has less immediate traffic but incurs complexity of dirty bit/cache line.
Virtual memory systems are write-back.
“write-allocate loads the corresponding block from the next lower level into the cache and then updates the cache block. Write-allocate tries to exploit spatial locality
of writes, but it has the disadvantage that every miss results in a block transfer from the next lower level to cache. The alternative, known as no-write-allocate,
bypasses the cache and writes the word directly to the next lower level. Write-through caches are typically no-write-allocate. Write-back caches are typically
write-allocate.”

## Slide 57: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain
  Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 58: Hardware Organization of a Computer System (Von Neumann)
General Architecture
L1
Cache
L2
Cache

## Slide 59: A Computer Memory Hierarchy
registers
on-chip L1
cache (SRAM)
L3 multi-core
shared cache (SRAM)
local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
remote secondary storage
(distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers.
L3 cache holds cache lines retrieved from main memory
off-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from the L2 cache memory.
CPU registers hold words retrieved from L1 cache.
L2 cache holds cache lines retrieved from L3 cache.
L0:
L1:
L2:
L3:
L5:
L6:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
main memory
(DRAM)
L4:
Main memory holds disk
blocks retrieved from local
disks.
Notes: L1 = tens of KB
L2 = hundreds of KB
L3 = MBs

## Slide 60: Memory Mountain Test Function
/* The test function */
void test(int elems, int stride) {
int i, result = 0;
volatile int sink;
for (i = 0; i < elems; i += stride)
result += data[i];
sink = result; /* So compiler doesn't optimize away the loop */
}
/* Run test(elems, stride) and return read throughput (MB/s) */
double run(int size, int stride, double Mhz)
{
double cycles;
int elems = size / sizeof(int);
test(elems, stride); /* warm up the cache first! */
cycles = fcyc2(test, elems, stride, 0); /* call test(elems,stride) */
return (size / stride) / (cycles / Mhz); /* convert cycles to MB/s */
}
Notes: volatile tells the C compiler to not optimize away any tests using the variable declared as volatile, in this case ‘sink’.
We assume data[] array is defined somewhere else as a global variable.

## Slide 61: Memory Mountain Main Routine
/* mountain.c - Generate the memory mountain. */
#define MINBYTES (1 << 10) /* Working set size ranges from 1 KB */
#define MAXBYTES (1 << 23) /* ... up to 8 MB */
#define MAXSTRIDE 16 /* Strides range from 1 to 16 */
#define MAXELEMS MAXBYTES/sizeof(int)
int data[MAXELEMS]; /* The array we'll be traversing */
int main()
{
int size; /* Working set size (in bytes) */
int stride; /* Stride (in array elements) */
double Mhz; /* Clock frequency */
init_data(data, MAXELEMS); /* Initialize each element in data to 1 */
Mhz = mhz(0); /* Estimate the clock frequency */
for (size = MAXBYTES; size >= MINBYTES; size >>= 1) {
for (stride = 1; stride <= MAXSTRIDE; stride++)
printf("%.1f\t", run(size, stride, Mhz));
printf("\n");
}
exit(0);
}

## Slide 62: The Memory Mountain

## Slide 63: Ridges of Temporal Locality
Slice through the memory mountain with stride=1
  illuminates read throughputs of different caches and memory
Notes: Since the cache is warmed up by calling test() a first time, before calling test() a second time to measure read throughput, then the first time test() is called, the 512 KB L2 cache can store the entire set of accessed data[] if the amount of data[] is < 512 KB, which is true for the L2 cache region. If the amount of data[] array is < size of L1 cache, then the L1 cache can store all data[] in the warm-up phase, which will then be readily accessible in the measurement phase. So we see temporal locality when the second set of accesses references the same data as the first set of accesses (warm-up).

## Slide 64: A Slope of Spatial Locality
Slice through memory mountain with size=256KB
  shows cache block size.

## Slide 65: Chapter 6: Cache Blocking and Hierarchy
Topics:
  Blocking Application Data to Improve Temporal Locality
  Caching in the memory hierarchy
  Magnetic vs Solid-state Drives

## Slide 66: Matrix Multiplication
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i][j] += a[i][k] * b[k][j];
}
By rearranging loop indices, exploit spatial locality
  e.g. Stride-1
  inner loop does not reuse the same data well, which is needed to exploit temporal locality
    Once done with b’s column j, don’t reuse it, move on to column j+1
Multiply in a way that exploits temporal locality, i.e. reuses the same data
  2-Dim Blocking

## Slide 67: Total Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 misses (from a[])
  + n misses (from b[],
  which is stride-N)
  = 9n/8 misses
  Afterwards in cache: (schematic)
*
=
n
*
=
8 wide
a[]
matrix
b[]
matrix
c[]
matrix

## Slide 68: Total Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 * n2 = (9/8) * n3 -- can we do better?
n
*
=
8 wide

## Slide 69: Improving Temporal Locality by Blocking
Organize your application data into chunks that fit in L1 cache, and are read/written together, then load the next related chunks, etc. – exploit temporal locality
  Example: Row*Column approach to matrix multiplication has poor temporal locality
*
=
8 wide
n
a submatrix
b
submatrix
i1
*
c (partial product)
=
  Instead, divide matrix into
  small chunks/submatrices,
  cache them, multiply them
  block by block, then discard
    Rows & columns of submatrices reused – temporal locality
  Working set size of row (and column) >> cache size, so keep getting misses
  Essentially, reduce size of submatrices until they all fit entirely in L1 cache
Notes: When we looked at matrix multiplication and permuted the order of the three loops I, j, and k, we found that j as inner loop achieved the lowest miss rate by exploiting spatial locality. However, even with j on the inner loop, we still have limited temporal locality, since once two elements are multiplied together in the inner loop, they are not needed again by the inner loop for that i and k. We’d like to organize the data so that elements are reused/re-referenced by the inner loop, which would take advantage of both spatial and temporal locality.

## Slide 70: Improving Temporal Locality by Blocking
Example: Blocked matrix multiplication
  “block” (in this context) does not mean “cache block”.
  Instead, it mean a sub-block within the application’s data matrix.
  Example: N = 8; sub-block size = 4
C11 = A11B11 + A12B21 C12 = A11B12 + A12B22
C21 = A21B11 + A22B21 C22 = A21B12 + A22B22
A11 A12
A21 A22
B11 B12
B21 B22
X
=
C11 C12
C21 C22
Key idea: Sub-blocks (i.e., Axy) can be treated just like scalars.

## Slide 71: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=B) // i’th block row
for (j = 0; j < n; j+=B) // j’th block column
for (k = 0; k < n; k+=B) // k’th block of “vector” multiply
/* B x B mini matrix multiplications */
for (i1 = i; i1 < i+B; i++)
for (j1 = j; j1 < j+B; j++)
for (k1 = k; k1 < k+B; k++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
*
c
=
Block size B x B
i1
j1
Repeat for all i1,j1
Notes: Blocking should be seen as complementary to other techniques, such as reordering loops for stride-1 access on both interior arrays in the matrix multiplication. For example, in the above slide, we could reorder the i1, j1, and k1 loops so that both arrays ‘a’ and ‘b’ are accessed in stride-1 sequence in the interior loop (of 6!).

## Slide 72: Total Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
    Three submatrices of a, b and c
First (block) iteration:
  B2/8 misses for each
  block =
  B/8 misses/row * B rows
  Total # misses per block of product matrix c
  = 2 * n/B * B2/8 = nB/4
  Afterwards in cache
  (schematic)
*
=
*
=
Block size B x B
n/B blocks
Notes: Matrix c is NxN and is the product matrix after multiplying NxN matrices a and b. Now, we’ve divided matric c into 2D blocks of size BxB. Let’s denote each 2D block of matric c as c{i}{j}, where the {i}{j} denote that we’re dealing with a block of matrix c in the I’th “block row” of c and the j’th “block column of c (rather than a particular [i][j]’th element of matrix c). Then to compute each block of the product matrix c{i}{j} = SUM a{i}{k}*b{k}{j}, where k=0 to N/B - 1. That is, each block of matrix c is the multiplication of the I’th “block row” of matrix a with the j’th “block column” of matrix b. Or we can say each block of matrix c is the inner product of the the I’th “block row” of matrix a with the j’th “block column” of matrix b. To calculate c{i}{j}, we need all the blocks from the I’th block row of matrix a, and all the blocks from the j’th block column of matrix b. That is we need blocks a{i}{0}, a{i}{1}, a{i}{2}, …, a{i}{N/B}, as well as b{0}{j}, b{1}{j}, b{2}{j},…, b{N/B}{j}. There are 2*N/B such blocks. Each such block will incur (B^2)/8 misses. So the total # misses for each c{i}{j} block is 2*N/B * (B^2)/8.

## Slide 73: Total Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Second (block) iteration:
  Same as first iteration
  2n/B * B2/8 = nB/4
Total misses:
  nB/4 * (n/B)2 = n3/(4B)
*
=
Block size B x B
n/B blocks

## Slide 74: Summary
No blocking: (9/8) * n3
Blocking: 1/(4B) * n3
Suggest largest possible block size B, but limit 3B2 < C! (can possibly be relaxed a bit, but there is a limit for B)
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array elements used O(n) times!
  But program has to be written properly
Notes: No blocking = (n/8 misses horizontally on a row + n misses vertically down a column)*n^2 = 9/8 * n^3

## Slide 75: Pentium Blocked Matrix Multiply Performance
Blocking (bijk and bikj) improves performance by a factor of two over unblocked versions (ijk and jik)
  relatively insensitive to array size.
Notes: The very best spatial-locality-only approach can be improved by adding blocking, which improves temporal locality, resulting in a ~2X speedup over the best spatial-locality-only approach.

## Slide 76: A Computer Memory Hierarchy
registers
on-chip L1
cache (SRAM)
L3 multi-core
shared cache (SRAM)
local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
remote secondary storage
(distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers.
L3 cache holds cache lines retrieved from main memory
off-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from the L2 cache memory.
CPU registers hold words retrieved from L1 cache.
L2 cache holds cache lines retrieved from L3 cache.
L0:
L1:
L2:
L3:
L5:
L6:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
main memory
(DRAM)
L4:
Main memory holds disk
blocks retrieved from local
disks.
Notes: L1 = tens of KB
L2 = hundreds of KB
L3 = MBs

## Slide 77: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
  Net effect: A large pool of memory that costs only slightly more than the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 78: Magnetic Disk Geometry
Disks consist of platters, each with two surfaces.
surface 0
surface 1
surface 2
surface 3
surface 4
surface 5
cylinder k
spindle
platter 0
platter 1
platter 2

## Slide 79: Magnetic Disk Geometry
Each surface consists of concentric rings called tracks.
Each track consists of sectors separated by gaps.
spindle
surface
tracks
track k
sectors
gaps
Total disk capacity = # platters* # surfaces/platter * # tracks/surface
* # sectors/track * # bits/sector

## Slide 80: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
spindle
By moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.

## Slide 81: Disk Access Time
Average time to access some target sector approximated by :
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tavg seek)
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek = 9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under r/w head.
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min (~ ms as well)
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min. (typically small)
Hence magnetic disks are slow (~ ms)!

## Slide 82: Solid State Disks (SSDs)
  Based on flash memory – all electronic, no mechanical parts
  Divided into B blocks, with P pages/block
  Reads are straightforward (~30 μs), but writes are more complicated (~300 μs)
  Flash blocks can wear out => do wear leveling

## Slide 83: Memory Hierarchy: Intel Core i7
Main Memory
Magnetic or Solid State Disk
L3 Shared Cache
16-way associative
L2 unified cache
8-way set associative
L1
I-cache 8-way
L1
D-cache 8-way
CPU
Reg
Latency:
30-40 cycles
11 cycles
4 cycles
millions
~256 KB
32 KB
~8 MB
~4 GB
Not drawn to scale
L1/L2/L3 caches: 64 B blocks
~500 GB
100 cycles
32 KB
For each Core (4):
Notes: Suppose CPU wants to read. Check L1 cache first. If hit, return read data immediately. Else check L2. If hit, return data to L1 (update L1) and then return data to CPU. Else check L3. If hit, return data to L2 (update L2) then return data to L1 (update L1) then return data to CPU. Else read data from memory and update caches L3, L2, and L1 in that order and then return data from L1 to CPU. What about writes? (see next slide) Note with writes that we have now inconsistency between the version of some piece of data cached (in L1, L2, and/or L3) and the version of the same data that is stored in main memory.

## Slide 84: Memory Hierarchy: Intel Core i7
Main Memory
Disk
L3 Shared Cache
16-way associative
L2 unified cache
8-way set associative
L1
I-cache 8-way
L1
D-cache 8-way
CPU
Reg
Latency:
30-40 cycles
11 cycles
4 cycles
millions
~256 KB
32 KB
~8 MB
~4 GB
Not drawn to scale
L1/L2/L3 caches: 64 B blocks
~500 GB
100 cycles
32 KB
For each Core (4):

## Slide 85: Intel Core i7
circa 2008

## Slide 86: Concluding Observations
Programmer can optimize for cache performance
  How data structures are organized
  How data are accessed
    Nested loop structure
    Blocking is a general technique
All systems favor “cache friendly code”
  Getting absolute optimum performance is very platform specific
    Cache sizes, line sizes, associativities, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small, e.g. use blocking to exploit temporal locality!
    Use small strides to exploit spatial locality!

## Slide 87: Chapter 6 Supplementary Slides

## Slide 88: Conventional DRAM Organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
memory
controller
(to CPU)

## Slide 89: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
cols
rows
RAS = 2
0
1
2
3
0
1
2
internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
memory
controller
Step 1(b): Row 2 copied from DRAM array to row buffer.

## Slide 90: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
internal buffer
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
memory
controller
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
supercell
(2,1)
supercell
(2,1)
To CPU
This two-phase
access to
memory adds
latency but
reduces the #
of address pins

## Slide 91: Memory Modules
: supercell (i,j)
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit doubleword at main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit doubleword
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit doubleword at main memory address A
Fast parallel data access

## Slide 92: Enhanced DRAMs
All enhanced DRAMs are built around the conventional DRAM core.
  Fast page mode DRAM (FPM DRAM)
    Access contents of row with [RAS, CAS, CAS, CAS, CAS] instead of [(RAS,CAS), (RAS,CAS), (RAS,CAS), (RAS,CAS)].
  Extended data out DRAM (EDO DRAM)
    Enhanced FPM DRAM with more closely spaced CAS signals.
  Synchronous DRAM (SDRAM)
    Driven with rising clock edge instead of asynchronous control signals.
  Double data-rate synchronous DRAM (DDR SDRAM)
    Enhancement of SDRAM that uses both clock edges as control signals.
  Video RAM (VRAM)
    Like FPM DRAM, but output is produced by shifting row buffer
    Dual ported (allows concurrent reads and writes)

## Slide 93: Nonvolatile Memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off.
  Generic name is read-only memory (ROM).
  Misleading because some ROMs can be read and modified.
Types of ROMs
  Programmable ROM (PROM)
  Eraseable programmable ROM (EPROM)
  Electrically eraseable PROM (EEPROM)
  Flash memory
Firmware
  Program stored in a ROM
    Boot time code, BIOS (basic input/ouput system)
    graphics cards, disk controllers.

## Slide 94: I/O Bus
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
Expansion slots for
other devices such
as network adapters.

## Slide 95: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte and have less capacity.
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 96: Examples of Caching in the Hierarchy
Hardware
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB page
64-bytes block
64-bytes block
4-byte words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
1
On-Chip L1
Hardware
10
Off-Chip L2
AFS/NFS client
10,000,000
Local disk
Hardware+OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?

## Slide 97: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware.
  Hold frequently accessed blocks of main memory
CPU looks first for data in L1, then in L2, then in main memory.
Typical bus structure:
main
memory
I/O
bridge
bus interface
L2 cache
ALU
register file
CPU chip
cache bus
system bus
memory bus
L1
cache

## Slide 98: Typical Bus Structure Connecting CPU and Memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus

## Slide 99: Memory Read Transaction (1)
CPU places address A on the memory bus.
ALU
register file
bus interface
A
0
A
x
main memory
I/O bridge
%eax
Load operation: movl A, %eax

## Slide 100: Memory Read Transaction (2)
Main memory reads A from the memory bus, retreives word x, and places it on the bus.
ALU
register file
bus interface
x
0
A
x
main memory
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 101: Memory Read Transaction (3)
CPU read word x from the bus and copies it into register %eax.
x
ALU
register file
bus interface
x
main memory
0
A
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 102: Memory Write Transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
y
ALU
register file
bus interface
A
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 103: Memory Write Transaction (2)
CPU places data word y on the bus.
y
ALU
register file
bus interface
y
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 104: Memory Write Transaction (3)
Main memory read data word y from the bus and stores it at address A.
y
ALU
register file
bus interface
y
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 105: Multi-Level Caches
Options: separate data and instruction caches, or a unified cache
size:
speed:
$/Mbyte:
line size:
200 B
3 ns
8 B
8-64 KB
3 ns
32 B
128 MB DRAM
60 ns
$1.50/MB
8 KB
30 GB
8 ms
$0.05/MB
larger, slower, cheaper
Memory
L1
d-cache
Regs
Unified
L2
Cache
Processor
1-4MB SRAM
6 ns
$100/MB
32 B
L1
i-cache
disk

## Slide 106: Intel Pentium Cache Hierarchy
Processor Chip
L1 Data
1 cycle latency
16 KB
4-way assoc
Write-through
32B lines
L1 Instruction
16 KB, 4-way
32B lines
Regs.
L2 Unified
128KB--2 MB
4-way assoc
Write-back
Write allocate
32B lines
Main
Memory
Up to 4GB

## Slide 107: Memory Hierarchy: Core 2 Duo
Disk
Main Memory
L2 unified cache
L1
I-cache
L1
D-cache
CPU
Reg
2 B/cycle
8 B/cycle
16 B/cycle
1 B/30 cycles
Throughput:
Latency:
100 cycles
14 cycles
3 cycles
millions
~4 MB
32 KB
~4 GB
~500 GB
Not drawn to scale
L1/L2 cache: 64 B blocks

## Slide 108: Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 B = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_cols(double a[16][16])
{
int i, j;
double sum = 0;
for (j = 0; i < 16; i++)
for (i = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
blackboard
Ignore the variables sum, i, j

## Slide 109: Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 B = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (j = 0; i < 16; i++)
for (i = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
blackboard
Ignore the variables sum, i, j

## Slide 110: Pentium Matrix Multiply Performance
Miss rates are helpful but not perfect predictors.
    Code scheduling matters, too.
Worse!

## Slide 111: Blocked Matrix Multiply (bijk)
for (jj=0; jj<n; jj+=bsize) {
for (i=0; i<n; i++)
for (j=jj; j < min(jj+bsize,n); j++)
c[i][j] = 0.0;
for (kk=0; kk<n; kk+=bsize) {
for (i=0; i<n; i++) {
for (j=jj; j < min(jj+bsize,n); j++) {
sum = 0.0
for (k=kk; k < min(kk+bsize,n); k++) {
sum += a[i][k] * b[k][j];
}
c[i][j] += sum;
}
}
}
}

## Slide 112: Blocked Matrix Multiply Analysis
  Innermost loop pair multiplies a 1 X bsize sliver of A by a bsize X bsize block of B and accumulates into 1 X bsize sliver of C
  Loop over i steps through n row slivers of A & C, using same B
A
B
C
block reused n times in succession
row sliver accessed
bsize times
Update successive
elements of sliver
i
i
kk
kk
jj
jj
for (i=0; i<n; i++) {
for (j=jj; j < min(jj+bsize,n); j++) {
sum = 0.0
for (k=kk; k < min(kk+bsize,n); k++) {
sum += a[i][k] * b[k][j];
}
c[i][j] += sum;
}
Innermost
Loop Pair

## Slide 113: Optimizations for the Memory Hierarchy
Write code that has locality
  Spatial: access data contiguously
  Temporal: make sure access to the same data is not too far apart in time
How to achieve?
  Proper choice of algorithm
  Loop transformations
Cache versus register level optimization:
  In both cases locality desirable
  Register space much smaller + requires scalar replacement to exploit temporal locality
  Register level optimizations include exhibiting instruction level parallelism (conflicts with locality)

## Slide 114: Inserting an L1 Cache Between the CPU and Main Memory
a b c d
block 10
p q r s
block 21
...
...
w x y z
block 30
...
The big slow main memory
has room for many 4-word
blocks.
The small fast L1 cache has room
for two 4-word blocks.
The tiny, very fast CPU register file
has room for four 4-byte words.
The transfer unit between
the cache and main
memory is a 4-word block
(16 bytes).
The transfer unit between
the CPU register file and
the cache is a 4-byte block.
line 0
line 1

## Slide 115: General Org of a Cache Memory
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set 0:
B = 2b bytes
per cache block
E lines
per set
S = 2s sets
t tag bits
per line
1 valid bit
per line
Cache size: C = B x E x S data bytes
• • •
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set 1:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set S-1:
• • •
• • •
Cache is an array
of sets.
Each set contains
one or more lines.
Each line holds a
block of data.

## Slide 116: Addressing Caches
t bits
s bits
b bits
0
m-1
<tag>
<set index>
<block offset>
Address A:
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set 0:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set 1:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set S-1:
• • •
• • •
The word at address A is in the cache if
the tag bits in one of the <valid> lines in
set <set index> match <tag>.
The word contents begin at offset
<block offset> bytes from the beginning
of the block.

## Slide 117: Direct-Mapped Cache
Simplest kind of cache
Characterized by exactly one line per set.
valid
valid
valid
tag
tag
tag
• • •
set 0:
set 1:
set S-1:
E=1 lines per set
cache block
cache block
cache block

## Slide 118: Accessing Direct-Mapped Caches
Set selection
  Use the set index bits to determine the set of interest.
valid
valid
valid
tag
tag
tag
• • •
set 0:
set 1:
set S-1:
t bits
s bits
0 0 0 0 1
0
m-1
b bits
tag
set index
block offset
selected set
cache block
cache block
cache block

## Slide 119: Accessing Direct-Mapped Caches
Line matching and word selection
  Line matching: Find a valid line in the selected set with a matching tag
  Word selection: Then extract the word
1
t bits
s bits
100
i
0110
0
m-1
b bits
tag
set index
block offset
selected set (i):
(3) If (1) and (2), then
cache hit,
and block offset
selects
starting byte.
=1?
(1) The valid bit must be set
= ?
(2) The tag bits in the cache
line must match the
tag bits in the address
0110
w3
w0
w1
w2
3
0
1
2
7
4
5
6

## Slide 120: Set Associative Caches
Characterized by more than one line per set
valid
tag
set 0:
E=2 lines per set
set 1:
set S-1:
• • •
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block

## Slide 121: Accessing Set Associative Caches
Set selection
  identical to direct-mapped cache
valid
valid
tag
tag
set 0:
valid
valid
tag
tag
set 1:
valid
valid
tag
tag
set S-1:
• • •
t bits
s bits
0 0 0 0 1
0
m-1
b bits
tag
set index
block offset
Selected set
cache block
cache block
cache block
cache block
cache block
cache block

## Slide 122: Accessing Set Associative Caches
Line matching and word selection
  must compare the tag in each valid line in the selected set.
1
0110
w3
w0
w1
w2
1
1001
t bits
s bits
100
i
0110
0
m-1
b bits
tag
set index
block offset
selected set (i):
=1?
(1) The valid bit must be set.
= ?
(2) The tag bits in one
of the cache lines must
match the tag bits in
the address
(3) If (1) and (2), then
cache hit, and
block offset selects
starting byte.
3
0
1
2
7
4
5
6

## Slide 123: Software Caches are More Flexible
Examples
  File system buffer caches, web browser caches, etc.
Some design differences
  Almost always fully associative
    so, no placement restrictions
    index structures like hash tables are common
  Often use complex replacement policies
    misses are very expensive when disk or network involved
    worth thousands of cycles to avoid them
  Not necessarily constrained to single “block” transfers
    may fetch or write-back in larger units, opportunistically