## Slide 1: Chapter 2: Integer Multiplication, Division and Byte Order/Endianness
Topics
  Casting between signed and unsigned integers
  Sign extension
  Integer multiplication
  Integer division
  Byte Ordering: Little vs Big Endian
    Ints
    Pointers
    Characters
    Strings
See last week’s
slides

## Slide 2: Announcements
Data Lab is due Friday Sept 13 by 11:55 pm
  Grading interview time slots released probably Friday – sign up for 12-minute slots that are spread over next week M-F
  Checked with anti-plagiarism software, so do your own work
Upcoming assignments
  Next Assembly Quiz will be released soon
  Bomb Lab #2 released soon, then due 3 weeks after that
Read Chapter 3.1-3.12 (except 3.11) and do practice problems

## Slide 3: Recap
Bitwise logic: &, |, ^, and ~
Logical operators: &&, ||, and !
Bit shifting
  Corresponds to multiplication and division by powers of two
Signed and unsigned binary encodings of integers
  Two’s complement
Two’s complement and unsigned overflow

## Slide 4: Unsigned Power-of-2 Divide with Shift
Quotient of Unsigned by Power of 2
  u >> k gives  u / 2k   “floor” function or RoundDown
  Uses logical shift
0
0
1
0
0
0
•••
2k
/
•••
k
u
Operands:
•••
•••
Binary Point
u / 2k
Division:
•••
0
•••
•••
.
 u / 2k 
•••
Result:
0
•••
Notes: Floor(x) = largest integer not greater than x.
Note that the yellow “MS bits” region does not necessarily align up after shifting with the green shifting bit, which the picture could be misinterpreted to imply. For example, if k is large, then the yellow region will be small. After shifting (u/2^k), the yellow region will be far to the right, while the green shifting bit will be far to the left – the difference would then be clear. Similarly, if k is small, then the yellow region will be large. After shifting, the upper edge of the yellow blocks will be on the far left, whereas the position of the green shifting bit will be to the far right – again the difference would be clear.

## Slide 5: Signed Power-of-2 Divide with Shift
Quotient of Signed by Power of 2
  x >> k gives  x / 2k 
  Uses arithmetic shift
  Rounds wrong direction when x < 0
0
0
1
0
0
0
•••
2k
/
•••
k
x
Operands:
•••
•••
Binary Point
x / 2k
Division:
•••
0
•••
•••
.
RoundDown(x / 2k)
•••
Result:
0
•••
Need to add one!
Notes: We also need to not add one when the division is exact and there is no remainder to throw away to the right of the binary point.

## Slide 6: Correct Power-of-2 Divide
Quotient of Negative Number by Power of 2
  Want  x / 2k  (Round Toward 0)  “ceiling” function
  Compute as  (x+2k-1)/ 2k 
    Adding a pre-bias 2k - 1
    In C: (x + (1<<k)-1) >> k
    Biases dividend toward 0
Case 1: No rounding
Divisor:
0
0
1
0
0
0
•••
2k
/
•••
k
0
0
0
1
1
1
•••
+2k +–1
•••
    Biasing has no effect
Dividend:
x
1
•••
0
0
0
•••
1
1
•••
1
1
1
•••
1
 x / 2k 
1
•••
0
1
1
•••
.
Binary Point
1
1
1
1
•••
1
1
1
1
…
Notes: Ceiling(x) = smallest integer not less than x

## Slide 7: Correct Power-of-2 Divide (Cont.)
Case 2: Rounding
Divisor:
0
0
1
0
0
0
•••
2k
/
•••
    Biasing adds the desired 1 to final result
k
Dividend:
x
1
•••
•••
0
0
0
1
1
1
•••
+2k +–1
•••
1
1
•••
•••
Incremented by 1
1
 x / 2k 
1
•••
0
1
1
•••
.
Binary Point
1
•••
Incremented by 1
1
1
1
1

## Slide 8: In C, Signed 2k Division via >>
The default for >> is RoundDown() or the Floor function
  Either positive or negative
  Imprecision for RoundDown for negative #’s
To get RoundToZero() rounding in signed 2k Division, you have to implement the following C code:
  (x<0 ? x+(1<<k)-1 : x) >> k
  This is equivalent to:
  If (x<0) {
  quotient = (x+2k – 1) >> k /* pre-bias by 2k – 1 before
  right-shifting*/
  } else { /* x >= 0 */
  quotient = x >> k
  }

## Slide 9: No Shortcuts to General Integer Division
Example: 117/37
  = 117/(25 + 22 + 20) ≠ 117/25 + 117/22 + 117/20
  Cannot distribute the division, unlike the multiplication
  So we cannot easily use a sum of right shifts as a shortcut for general integer division
Special hardware circuits are designed to implement an integer division
  Access these integer division circuits by invoking the appropriate assembly language instruction, e.g. idivl

## Slide 10: Byte Ordering
In what order should bytes within a multi-byte word be stored in memory?
  Consider a 32-bit integer or int (4 bytes)
  0000 0001 0010 0011 0100 0101 0110 01112
  = 0x 0 1 2 3 4 5 6 7
  = 0x 01 23 45 67
Most
Significant
Byte (MSB)
Least
Significant
Byte (LSB)
  In what order do we store these four bytes 0x01234567 in memory, say at starting address 12?
    Little Endian approach: Least significant byte has lowest address (12), followed by the next least significant byte in the next lowest address (13), etc. – i.e. “little end first”
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
Memory
(bytes)
Addr.
0003
0002
0001
0000
0x67
0x45
0x23
0x01
Little
Endian

## Slide 11: Byte Ordering Example
Big Endian
  Most significant byte has lowest address, i.e. “big end first”
Little Endian
  Least significant byte has lowest address
Example
  Variable x has 4-byte representation 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01
Notes: Bit order usually follows the same endianness as the byte order for a given computer system. That is, in a big endian system the most significant bit is stored at the lowest bit address; in a little endian system, the least significant bit is stored at the lowest bit address. – from Linux Journal

## Slide 12: Byte Ordering in Hardware
Aside: Endianness came from Gulliver’s Travels
CPU Conventions
  Sun SPARC, Motorola 68K, Power PC (PPC’s) are “Big Endian” machines
    Most significant byte has lowest address
  ISA64 are “Little Endian” machines
    Least significant byte has lowest address
  Some are “bi-endian” (hardware supports both types of Endianness, which can improve performance)
    MIPS, Alpha, ARM
Notes: For bi-endian, have to tell CPU hardware when to use which endianness. Applies primarily to data, though some systems also support bi-endianness for code.

## Slide 13: Reading Byte-Reversed Listings
Disassembly
  Text representation of binary machine code
  Generated by program that reads the machine code
Example Fragment
Address Instruction Code Assembly Rendition
8048365: 5b pop %ebx
8048366: 81 c3 ab 12 00 00 add $0x12ab,%ebx
804836c: 83 bb 28 00 00 00 00 cmpl $0x0,0x28(%ebx)
Deciphering Numbers
  Value: 0x12ab
  Pad to 4 bytes: 0x000012ab
  Split into bytes: 00 00 12 ab
  Reverse: ab 12 00 00
So this is
Little Endian
Notes: Note how the instruction codes are variable length. To handle this, the CPU reads the first byte of the next instruction. This will contain escape sequences that indicate how many additional bytes may need to be read, if any. In the common case, frequently used instructions will be handled by the first byte, but for other less commonly used instructions, additional memory accesses may be needed to fetch the remainder of the opcode.

## Slide 14: Examining Data Representations
Code to Print Byte Representation of Data
  Casting pointer to unsigned char * creates byte array
typedef unsigned char *pointer;
void show_bytes(pointer start, int len)
{
int i;
for (i = 0; i < len; i++)
printf("0x%p\t0x%.2x\n",
start+i, start[i]);
printf("\n");
}
Printf directives:
  %p: Print pointer
  %x: Print Hexadecimal
equivalent to *(start+i)
Use show_bytes() to find if your machine is Little Endian or Big Endian
Notes: Note the typedef defines type pointer as an unsigned char *. Then, “pointer start” casts any input pointer to type unsigned char *. This means that within the loop, (start+i) is incremented by one byte each time, since start is a pointer to an unsigned char (one byte wide). This then allows us to print the data pointed to by any input pointer a byte at a time, which is what we want. If we failed to cast the input pointer to an unsigned char *, then (start + i) within the loop would actually increment the pointer by start+i*sizeof(start). For example, if we called show_bytes with an int* pointer ip, namely show_bytes(ip,sizeof(ip)), where sizeof(ip)=4, and if we didn’t cast start to be an unsigned char * (i.e. it stays as an int* pointer), then (start+i) would actually be compiled into code that is incremented by start+i*4 each time, which would print a byte and skip the next 3 bytes. This is not what is desired.

## Slide 15: show_bytes Execution Example
int a = 15213; // = 0x3B6D
printf("int a = 15213;\n");
show_bytes((pointer) &a, sizeof(int));
Result (Linux):
int a = 15213;
0x11ffffcb8 0x6d
0x11ffffcb9 0x3b
0x11ffffcba 0x00
0x11ffffcbb 0x00
Little Endian with zero padding in most significant bytes

## Slide 16: Endianness and Arrays
Integer Array Example:
int S[3];
S[0] = 410; /* = 0x0000019a */
S[1] = 14; /* = 0x0000000d */
S[2] = 4099; /* = 0x00001003 */
  Let the int array S be stored starting at memory address 4
  Lowest element of array S[0] is stored starting at the lowest address of the array (byte 4)
    Next lowest element of array S[1] is stored at the next lowest memory address of int array (byte 8). And so on…
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
Memory
(bytes)
Addr.
0003
0002
0001
0000
0x00
0x00
0x10
0x03
0x00
0x00
0x00
0x0d
0x00
0x00
0x01
0x9a
S[0]
4 bytes
S[1]
4 bytes
S[2]
4 bytes
  Note how each int in the array is stored according to byte ordering rules (little endian)

## Slide 17: Endianness and Pointers
int B = -15213;
int *P = &B;
X64 Address (64-bit, higher order hex not shown)
Hex: 1 F F F F F C A 0
Binary: 0001 1111 1111 1111 1111 1111 1100 1010 0000
FF
FF
FC
A0
00
00
00
01
Alpha P
Different compilers & machines assign different locations to objects,
i.e. not only are the addresses stored in the pointer of different widths,
but they are also of different values (locations)
Little EndianLinux P
Linux Address (32-bit)
Hex: B F F F F 8 D 4 Binary: 1011 1111 1111 1111 1111 1000 1101 0100
F8
D4
BF
FF
Sun Address (32-bit)
Hex: E F F F F B 2 C Binary: 1110 1111 1111 1111 1111 1011 0010 1100
Big Endian Sun P
FF
EF
2C
FB
Low mem
High mem
Notes: This example illustrates several concepts at once. First, it shows that pointers have different sizes on different systems, e.g. 32 bits/4 bytes on 32-bit systems, and 64-bit/8 bytes wide on 64-bit systems. Second, it shows that once we have the width of a pointer defined on a system, that the bytes in that pointer must be laid out in memory according to some order, namely their endianness.

## Slide 18: Endianness and Floats
Float F = 15213.0;
IEEE Single Precision Floating Point Representation
Hex: 4 6 6 D B 4 0 0 Binary: 0100 0110 0110 1101 1011 0100 0000 0000
15213: 1110 1101 1011 01
Not same as integer representation, but consistent across machines
Can see some relation to integer representation, but not obvious
IEEE Single Precision Floating Point Representation
Hex: 4 6 6 D B 4 0 0 Binary: 0100 0110 0110 1101 1011 0100 0000 0000
15213: 1110 1101 1011 01
IEEE Single Precision Floating Point Representation
Hex: 4 6 6 D B 4 0 0 Binary: 0100 0110 0110 1101 1011 0100 0000 0000
15213: 1110 1101 1011 01
00
B4
6D
46
Big Endian
Sun F
B4
00
46
6D
Little Endian
Linux/Alpha F
Low mem
High mem

## Slide 19: Representing Characters
Actually unsigned characters, via ASCII (American Standard Code for Information Exchange)
The alphabet, numbers, punctuation, and symbols are encoded via an 8-bit ASCII table:
Example: numbers start with ‘0’ = 0x30, capital letters start at ‘A’ = 0x41 = 65, lower case letter ‘a’ = 0x61
Endianness doesn’t affect character representations
(hex)
Notes: Other larger encodings like UTF-8 exist in order to accommodate other alphabets and character sets like Cyrillic, Chinese, etc. UTF-8 is backwardly compatible with ASCII. Unicode is a 2-byte or 16-bit encoding standard.

## Slide 20: Representing Strings
char S[6] = "15213";
Strings in C
  Represented by array of characters
  Each character encoded in ASCII format
    ‘1’ = 0x31
    ‘5’ = 0x35
    ‘2’ = 0x32
    ‘1’ = 0x31
    ‘3’ = 0x33
  String should be null-terminated
    Final character = 0
Big Endian
Sun S
0x31
0x32
0x00
0x33
0x35
0x31
Little Endian
Linux/Alpha S
0x31
0x32
0x00
0x33
0x35
0x31
LO
HI
Compatibility
  Byte ordering not an issue
    Data are single byte quantities
  Text files generally platform independent
    Except for different conventions of line termination character(s)!
Notes: Note how arrays are stored starting with the lowest element of the array at the lowest memory (starting) address of the array. See the slide on Endianness and Arrays.

## Slide 21: Machine-Level Code Representation
Encode Program as Sequence of Instructions
  Each simple operation
    Arithmetic operation
    Read or write memory
    Conditional branch
  Instructions encoded as bytes
    Alpha’s, Sun’s, old Mac’s use 4 byte instructions
      Reduced Instruction Set Computer (RISC)
    PC’s new Mac’s use variable length instructions
      Complex Instruction Set Computer (CISC)
  Different instruction types and encodings for different machines
    Most code not binary compatible
Programs are Byte Sequences Too!

## Slide 22: Representing Instructions
int sum(int x, int y)
{
return x+y;
}
Different machines use totally different instructions and encodings
00
00
30
42
Alpha sum
01
80
FA
6B
E0
08
81
C3
Sun sum
90
02
00
09
  For this example, Alpha & Sun use two 4-byte instructions
    Use differing numbers of instructions in other cases
  PC uses 7 instructions with lengths 1, 2, and 3 bytes
    Same for NT and for Linux
    NT / Linux not fully binary compatible
E5
8B
55
89
PC sum
45
0C
03
45
08
89
EC
5D
C3
Notes: Code seems to be laid out big endian, ie if we look at an assembly instruction it is typically encoded left to right with the most important coding (of the instruction) on the left then any parameters on the right (registers, constants). Then it is stored with the most important codes stored in lower memory first. However, note that constants inside the instruction are encoded little endian on x86!

## Slide 23: Supplementary Slides

## Slide 24: Compiled Unsigned Division Code
shrq $3, %rax
Uses logical shift for unsigned
For Java Users
  Logical shift written as >>>
unsigned long udiv8
(unsigned long x)
{
return x/8;
}
# Logical shift
return x >> 3;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 25: Compiled Signed Division Code
testq %rax, %rax
js L4
L3:
sarq $3, %rax
ret
L4:
addq $7, %rax
jmp L3
Uses arithmetic shift for int
For Java Users
  Arith. shift written as >>
long idiv8(long x)
{
return x/8;
}
if x < 0
x += 7;
# Arithmetic shift
return x >> 3;
C Function
Compiled Arithmetic Operations
Explanation