## Slide 1: Chapter 3: Introduction to x86 Assembly Language
Topics
  Move operations to/from memory
  Addressing modes
  Arithmetic operations
  Condition Codes
  Conditional Jumping/Branching
  Loops

## Slide 2: Announcements
Data Lab grading this week
  Sign up for 12-minute slots, come prepared and don’t forget!
Next Assembly Quiz on moodle, due soon
Bomb Lab #2 released this week, due Friday Oct 4
Read Chapter 3.1-3.12 (except 3.11) and do practice problems

## Slide 3: Simple Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset
  movq 8(%rbp),%rdx
Go to memory address %rbp+8
and fetch the data located there

## Slide 4: Example of Simple Addressing Modes
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret
Notes: Midterm announcement, endian, extended time show up in my office 2-3:15 pm,

## Slide 5: C Pointers – A Quick Recap
int count=1;
  Declare an integer named count
  This allocates 4 bytes in memory for the variable count
  Initialize count to the value 1
char *p1;
  Declare p1 as a pointer to a char, i.e. the value of p1 is interpreted as a memory address (4 bytes wide on 32-bit systems)
  The pointer is allocated space in memory (4 bytes, not 1)
int *p2 = &count;
  Declare p2 as a pointer to an integer
  Allocates 4 bytes in memory for the pointer (32-bit)
  Initializes its value to the memory address of the count variable

## Slide 6: C Pointers (2)
  We see p2 storing the memory address of count, i.e. p2 is pointing at count
  p1 is uninitialized and not yet pointing at any character
Memory
(4 bytes wide)
Addresses:
0xFFC8
0xFFC4
0xFFC0
1
----
0xFFC0
p2
p1
count
0x0000
0xFFFF
int count=1;
char *p1;
int *p2 = &count;
  Assume the variables are laid out in memory as shown
  Assume a 32-bit system
For brevity, the two most significant
bytes of address are not shown
Notes: Note pointers are 32-bits or 4 bytes wide on 32-bit systems, which is the assumption in this slide
Pointers like p1 and p2 would be 64-bits or 8 bytes long on 64-bit systems.

## Slide 7: Understanding Swap()
%rdi
%rsi
%rax
%rdx
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Memory
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Registers

## Slide 8: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 9: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 10: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 11: Understanding Swap()
456
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 12: Understanding Swap()
456
123
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 13: Moving different word sizes
movq %rax, %rdx
  Move a “quad” word (4*16 = 64 bits = 8 bytes) from register %rax to register %rdx
movl %eax, %edx
  Move a “long” word (2*16 = 32 bits = 4 bytes) from register %eax to register %edx
movw %ax, %dx
  Move a word (16 bits = 2 bytes) from register %ax to register %dx
movb %al, %dl
  Move a byte from register %al to register %dl

## Slide 14: Indexed Addressing Modes
This means:
  Move a quad word (8 bytes) from the memory location %rdi + 4*%rsi + 24 to register %rax
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 16 integer registers
  Ri: Index register: Any, except for %rsp
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
movq 24(%rdi,%rsi,4), %rax

## Slide 15: Indexed Addressing Modes (2)
Special Cases
  (Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
    movq (%rax,%rbx), %rdx
  D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
    movq %rdx, 12(%rax,%rbx)
  (Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]
    movq (%rax,%rbx,8), %rdx
  (Rb) Mem[Reg[Rb]+S*Reg[Ri]]
    movq %rdx, (%rax)

## Slide 16: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x0100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 17: C operators – Assembly Equivalents?
Operators
() [] -> .
! ~ ++ -- + - * & (type) sizeof
* / %
+ -
<< >>
< <= > >=
== !=
&
^
|
&&
||
?:
= += -= *= /= %= &= ^= != <<= >>=
,
Many of these C operators have direct x86 assembly equivalents

## Slide 18: Some Arithmetic Operations
Two Operand Instructions:
  Format Computation
    addq Src,Dest Dest = Dest + Src
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
    salq Src,Dest Dest = Dest << Src Also called shlq
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    shrq Src,Dest Dest = Dest >> Src Logical
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
Watch out for argument order!
No distinction between signed and unsigned int (why?)
Notes: The text describes more assembly language arithmetic instructions, such as the complicated signed division idivl (uses two registers to store the input dividend, and the same two registers to store the output quotient and remainder), unsigned multiply mull, etc.
Just as for mov, we have many size variations of these instructions, e.g. addq, addl, addw, etc.

## Slide 19: Some Arithmetic Operations
One Operand Instructions
    incq Dest Dest = Dest + 1
    decq Dest Dest = Dest  1
    negq Dest Dest =  Dest
    notq Dest Dest = ~Dest
See book for more instructions

## Slide 20: lea Instruction for Address Computation
lea = “Load effective address”
leaq Src,Dest
  Src is indexed address mode expression
  Set Dest (must be register) to value denoted by expression
  Example:
  leaq 10(%rdx, %rdx, 4), %rax
  Therefore“%rax = 5 * %rdx + 10”
  Compare to:
  movq 10(%rdx, %rdx, 4), %rax
  means “%rax = Mem[5*%rdx + 10]
%rdx + 4*%rdx + 10
= 5*%rdx + 10

## Slide 21: lea Instruction for Address Computation
Uses
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8.
  Computing address without doing memory reference
    E.g., translation of p = &x[i];
long m12(long x)
{
return x*12;
}
leaq (%rdi,%rdi,2), %rax # t <- x+x*2
salq $2, %rax # return t<<2
Converted to ASM by compiler:
Example
Notes: Leaq and salq may be faster than an imulq, which wants to break 12 into a sum of powers of 2.

## Slide 22: Arithmetic Expression Example
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication
    But, only used once
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret

## Slide 23: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | t1, t2, rval
%rdx | t4
%rcx | t5
Notes: the computation for t3 is folded into the computation for t5

## Slide 24: Processor State (x86-64, Partial)
Information about currently executing program
  Temporary data ( %rax, … )
  Location of runtime stack ( %rsp )
Registers
Current stack top
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
%rip
Instruction pointer
  Location of current code control point ( %rip, … )
CF
ZF
SF
OF
Condition codes
  Status of recent tests ( CF, ZF, SF, OF )

## Slide 25: Condition Codes (Implicit Setting)
Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
Implicitly set (think of it as side effect) by arithmetic operations
  addq Src,Dest
  C analog: t = a+b
  CF set if carry out from most significant bit
    Used to detect unsigned overflow
  ZF set if t == 0
  SF set if t < 0 (as signed)
  OF set if two’s complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Codes set differently depending on instructions, and in some cases not set at all, e.g. lea instruction
Notes: OF corner case: why is t>=0 in the far-right expression? Answer: let a= largest neg # (4 bits) = ‘1000’, b=‘1000’, a+b=t=‘0000’=0, so must check t>=0, not just t>0.

## Slide 26: Condition Codes (Explicit Setting: Compare)
Explicit Setting by Compare Instruction
  cmpq Src2,Src1
  cmpq b,a like computing a-b without setting destination
  CF set if carry out from most significant bit (used for unsigned comparisons)
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  OF set if two’s complement (signed) overflow (a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)
Notes: Note how this differs from subq Src2, Src1, which would change the result in the destination register Src1. Cmpq doesn’t change the result in Src1, and only affects the condition codes.
Should that be (a-b)>=0 on the last test on the right side of the “OF set”, per the slide on addq setting the OF bit? If a-b=0, i.e. a=b, then we cannot have both a<0 and b>0.

## Slide 27: Condition Codes (Explicit Setting: Test)
Explicit Setting by Test instruction
  testq Src2,Src1 testq b,a like computing a&b without setting destination
  Sets condition codes based on value of Src1 & Src2
  Useful to have one of the operands be a mask
  ZF set when a&b == 0
  SF set when a&b < 0

## Slide 28: x86-64 Integer Registers
%rsp
  Can reference low-order byte
%al
%bl
%cl
%dl
%sil
%dil
%spl
%bpl
%r8b
%r9b
%r10b
%r11b
%r12b
%r13b
%r14b
%r15b
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 29: Reading Condition Codes
setX dest // e.g. setl %al
  Set low-order byte of destination to 0 or 1 based on combinations of condition codes
  Does not alter remaining 7 bytes
  Previous instruction should be a cmp
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (Signed)
setge | ~(SF^OF) | Greater or Equal (Signed)
setl | (SF^OF) | Less (Signed) – derivation in text
setle | (SF^OF)¦ZF | Less or Equal (Signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)
Notes: See p. 204 of text for explanation of how setl = (SF^OF).
Typically, we have a cmpq b,a preceding the set statement. Then for example a setl immediately following the cmpq will set the appropriate dest register if a<b. Note how the logic is reversed from intuition, which would tell us to set the reg if b<a. I think this is a byproduct of cmp staying consistent with the syntax of the sub instruction, which subtracts the first arg from the second arg.

## Slide 30: Reading Condition Codes (Cont.)
cmpq %rsi, %rdi # Compare x:y
  setg %al # Set when >
  movzbl %al, %eax # Zero rest of %rax
ret
SetX Instructions:
  Set single byte based on combination of condition codes
One of addressable byte registers
  Does not alter remaining bytes
  Typically use movzbl to finish job
    Also a movzbq, etc.
int gt (long x, long y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
Notes: %al are the lowest 8 bits(least significant) in the %eax register – see p.180in textbook.
movzbl = Move zero-extended byte to double word. The movzbl instruction clears the high-order 3 bytes of %eax.
Note %ax, %bx, %cx, and %dx are the lowest word in the %eax, %ebx, %ecx, and %edx registers respectively. Also %si and %di. Also %sp and %bp. See Figure 3.2 on p. 180.
    Note “32-bit instructions also set upper 32 bits to 0” (from textbook slides, commenting on movzbl)

## Slide 31: Jumping – Conditional
jX Instructions
  Conditional jumps to different part of code depending on condition codes, e.g. jle Label
  Critical for implementing if-then-else and for loops!
jX | Condition | Description
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 32: Jumping - Unconditional
jmp Label
  will encode the Label (address to jump to) as part of the jump instruction at compile time
jmp *%eax
  uses the value in register %eax at run time as the jump target
jmp *(%eax)
  reads the jump target from memory, using the value in %eax as the read address.
There is no jmp %eax or jmp (%eax) – compiler won’t generate this syntax.

## Slide 33: Conditional Branch Example (Old Style)
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
absdiff:
cmpq %rsi, %rdi # x:y
jle .L4
movq %rdi, %rax
subq %rsi, %rax
ret
.L4: # x <= y
movq %rsi, %rax
subq %rdi, %rax
ret
If-then-else converted to assembly form
Notes:   Generation gcc –Og -S –fno-if-conversion control.c

## Slide 34: Expressing with Goto Code
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
C allows goto statement
Jump to position designated by label
Generally considered bad programming practice
long absdiff_j
(long x, long y)
{
long result;
int ntest = x <= y;
if (ntest) goto Else;
result = x-y;
goto Done;
Else:
result = y-x;
Done:
return result;
}

## Slide 35: General Conditional Expression Translation (Using Branches)
C Code
val = Test ? Then_Expr : Else_Expr;
Goto Version
ntest = !Test;
if (ntest) goto Else;
val = Then_Expr;
goto Done;
Else:
val = Else_Expr;
Done:
. . .
  Test is expression returning integer
    = 0 interpreted as false
    0 interpreted as true
  Create separate code regions for then & else expressions
  Execute appropriate one
val = x>y ? x-y : y-x;

## Slide 36: Conditional Move
cmovX src, dest
  Set dest=src only if condition X holds
  More efficient than conditional branching for highly pipelined processors – easier to guess the next instruction to execute
  But overhead: both branches are evaluated
cmovX | Condition | Description
cmove | ZF | Equal / Zero
cmovne | ~ZF | Not Equal / Not Zero
cmovs | SF | Negative
cmovns | ~SF | Nonnegative
cmovg | ~(SF^OF)&~ZF | Greater (Signed)
cmovge | ~(SF^OF) | Greater or Equal (Signed)
cmovl | (SF^OF) | Less (Signed)
cmovle | (SF^OF)¦ZF | Less or Equal (Signed)
cmova | ~CF&~ZF | Above (unsigned)
cmovb | CF | Below (unsigned)
Notes: I believe cmov’s src must be a register while cmov’s dest can be either register or memory.

## Slide 37: Using Conditional Moves
C Code
val = Test
? Then_Expr
: Else_Expr;
Goto Version
result = Then_Expr;
eval = Else_Expr;
nt = !Test;
if (nt) result = eval;
return result;
Conditional Move Instructions
  Instruction supports:
    if (Test) Dest  Src
  Supported in post-1995 x86 processors
  GCC tries to use them
    But, only when known to be safe
Why?
  Branches are very disruptive to instruction flow through pipelines
  Conditional moves do not require control transfer

## Slide 38: Conditional Move Example
absdiff:
movq %rdi, %rax # x
subq %rsi, %rax # result = x-y
movq %rsi, %rdx
subq %rdi, %rdx # eval = y-x
cmpq %rsi, %rdi # x:y
cmovle %rdx, %rax # if <=, result = eval
ret
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 39: Bad Cases for Conditional Move
Expensive Computations
Both values get computed
Only makes sense when computations are very simple
val = Test(x) ? Hard1(x) : Hard2(x);
Risky Computations
Both values get computed
May have undesirable effects
val = p ? *p : 0;
Computations with side effects
Both values get computed
Must be side-effect free
val = x > 0 ? x*=7 : x+=3;

## Slide 40: Loops in C
do {
body-statement
} while (test-expr);
Executes body-statement
Then tests expression
  If true, loops back to ‘do’
  Else exit
while (test-expr) {
body-statement
}
Tests expression first
  If true, executes body & loops back to ‘while’
  Else exit
for(init; test; update) {
body-statement
}
Initializes first
If test is true
  Execute body statement
  Execute update & loop back to ‘for’
Else exit

## Slide 41: “Do-While” Loop Example
C Code
long pcount_do
(unsigned long x) {
long result = 0;
do {
result += x & 0x1;
x >>= 1;
} while (x);
return result;
}
Goto Version
long pcount_goto
(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Count number of 1’s in argument x (“popcount”)
Use conditional branch to either continue looping or to exit loop

## Slide 42: “Do-While” Loop Compilation
Goto Version
movl $0, %eax # result = 0
.L2: # loop:
movq %rdi, %rdx
andl $1, %edx # t = x & 0x1
addq %rdx, %rax # result += t
shrq %rdi # x >>= 1
jne .L2 # if (x) goto loop
rep; ret
long pcount_goto
(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Register | Use(s)
%rdi | Argument x
%rax | result

## Slide 43: General “Do-While” Translation
C Code
do
Body
while (Test);
Goto Version
loop:
Body
if (Test)
goto loop
Body:
{
Statement1;
Statement2;
…
Statementn;
}

## Slide 44: General “While” Translation #1
While version
while (Test)
Body
“Jump-to-middle” translation
Used with -Og
Goto Version
goto test;
loop:
Body
test:
if (Test)
goto loop;
done:

## Slide 45: While Loop Example #1
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Jump to Middle Version
long pcount_goto_jtm
(unsigned long x) {
long result = 0;
goto test;
loop:
result += x & 0x1;
x >>= 1;
test:
if(x) goto loop;
return result;
}
Compare to do-while version of function
Initial goto starts loop at test

## Slide 46: General “While” Translation #2
While version
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
“Do-while” conversion
Used with –O1
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 47: While Loop Example #2
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Do-While Version
long pcount_goto_dw
(unsigned long x) {
long result = 0;
if (!x) goto done;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
done:
return result;
}
Compare to do-while version of function
Initial conditional guards entrance to loop

## Slide 48: “For” Loop Form
for (Init; Test; Update )
Body
General Form
#define WSIZE 8*sizeof(int)
long pcount_for
(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
return result;
}
i = 0
i < WSIZE
i++
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
Init
Test
Update
Body

## Slide 49: “For” Loop  While Loop
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version

## Slide 50: For-While Conversion
long pcount_for_while
(unsigned long x)
{
size_t i;
long result = 0;
i = 0;
while (i < WSIZE)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
i++;
}
return result;
}
i = 0
i < WSIZE
i++
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
Init
Test
Update
Body

## Slide 51: “For” Loop Do-While Conversion
C Code
Initial test can be optimized away
long pcount_for
(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
return result;
}
Goto Version
long pcount_for_goto_dw
(unsigned long x) {
size_t i;
long result = 0;
i = 0;
if (!(i < WSIZE))
goto done;
loop:
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
i++;
if (i < WSIZE)
goto loop;
done:
return result;
}
Init
!Test
Body
Update
Test

## Slide 52: Switch Statements
Compact replacement for a long series of if – else if – else if - …
  Many if … else if ... else if’s ... are slow to evaluate due to many compares and conditional jumps
  Instead use a switch statement – good if many contiguous cases and switch argument is simple
    Contiguous needed to avoid sparse jump table
long switch_eg
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 53: Switch Statements
Special cases
  Multiple case labels: 5 & 6
  Fall through cases: 2
  Missing cases: 4 goes to default
long switch_eg
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 54: Switch Statements
Implemented as a Jump Table (array of addresses)
  Index into array and jump to branch target
  Avoids conditionals
  Good when cases are small integer constants
GCC picks one based on case structure
long switch_eg
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 55: Jump Table Structure
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
JTab:
switch(x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Jump Table
Jump Targets
target = Jtab[x];
goto *target;
Approx. Translation
Note: no conditional evaluation needed, so
very fast to jump to code block, but at cost of
a potentially large jump table

## Slide 56: Switch Statement Example
Setup:
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8
jmp *.L4(,%rdi,8)
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value
Indexes into jump table and
jumps to correct code block
Notes: Whenever you see such an assembly line, you should think switch statement (hint for bomb lab)

## Slide 57: Switch Statement Example
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
Indirect jump
Jump table
Setup:
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8 # Use default
jmp *.L4(,%rdi,8) # goto *JTab[x]
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6

## Slide 58: Assembly Setup Explanation
Table Structure
  Each target requires 8 bytes
  Base address at .L4
Jumping
  Direct: jmp .L8
  Jump target is denoted by label .L8
  Indirect: jmp *.L4(,%rdi,8)
  Start of jump table: .L4
  Must scale by factor of 8 (addresses are 8 bytes)
  Fetch target from effective Address (.L4 + x*8)
    Only for 0 ≤ x ≤ 6
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6

## Slide 59
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
case 5:
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
Jump Table

## Slide 60: Code Blocks (x == 1)
.L3:
movq %rsi, %rax # y
imulq %rdx, %rax # y*z
ret
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 61: Handling Fall-Through
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
case 3:
w = 1;
case 2:
w = y/z;
goto merge;
merge:
w += z;

## Slide 62: Code Blocks (x == 2, x == 3)
.L5: # Case 2
movq %rsi, %rax
cqto
idivq %rcx # y/z
jmp .L6 # goto merge
.L9: # Case 3
movl $1, %eax # w = 1
.L6: # merge:
addq %rcx, %rax # w += z
ret
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 63: Code Blocks (x == 5, x == 6, default)
.L7: # Case 5,6
movl $1, %eax # w = 1
subq %rdx, %rax # w -= z
ret
.L8: # Default:
movl $2, %eax # 2
ret
switch(x) {
. . .
case 5: // .L7
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 64: Sparse Switch Example
  Not practical to use jump table
    Would require 10000 entries!
    Most of entries in jump table are the same default
  Obvious translation into if-then-else would have maximum of 9 tests in the worst case
    Can we do better?
    Yes, use a tree-based approach – logarithmic in # tests (e.g. 4)
/* Return x/1111 if x is multiple
&& <= 9999. -1 otherwise */
int div1111(int x)
{
switch(x) {
case 0: return 0;
case 1111: return 1;
case 2222: return 2;
case 3333: return 3;
case 4444: return 4;
case 5555: return 5;
case 6666: return 6;
case 7777: return 7;
case 8888: return 8;
case 9999: return 9;
default: return -1;
}
}

## Slide 65: Supplementary Slides

## Slide 66: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 8(%ebp),%eax
xorl 12(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
movl %ebp,%esp
popl %ebp
ret
Body
Set
Up
Finish
movl 8(%ebp),%eax # eax = x
xorl 12(%ebp),%eax # eax = x^y
sarl $17,%eax # eax = t1>>17
andl $8185,%eax # eax = t2 & 8185

## Slide 67: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 8(%ebp),%eax
xorl 12(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
movl %ebp,%esp
popl %ebp
ret
Set
Up
Finish
movl 8(%ebp),%eax # eax = x
xorl 12(%ebp),%eax # eax = x^y (t1)
sarl $17,%eax # eax = t1>>17 (t2)
andl $8185,%eax # eax = t2 & 8185
Body

## Slide 68: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 8(%ebp),%eax
xorl 12(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
movl %ebp,%esp
popl %ebp
ret
Set
Up
Finish
movl 8(%ebp),%eax # eax = x
xorl 12(%ebp),%eax # eax = x^y (t1)
sarl $17,%eax # eax = t1>>17 (t2)
andl $8185,%eax # eax = t2 & 8185
Body

## Slide 69: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 8(%ebp),%eax
xorl 12(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
movl %ebp,%esp
popl %ebp
ret
Set
Up
Finish
movl 8(%ebp),%eax # eax = x
xorl 12(%ebp),%eax # eax = x^y (t1)
sarl $17,%eax # eax = t1>>17 (t2)
andl $8185,%eax # eax = t2 & 8185
213 = 8192, 213 – 7 = 8185
Body
Note how
compiler
combines
2 source code
lines into 1

## Slide 70: Example: Left Shifting <<
shl or sal
How are condition flags set?
  shl/sal sets carry flag to last shifted out bit.
    For unsigned, if CF=1, then overflow occurred.
  for overflow flag OF,
    if shift by one,
      if CF & MSbit identical after shift, OF = 0
      else OF = 1 (MS bit changes from 1->0 or 0->1),
      i.e. OF = CF ^ MSbit
    else if shift by > 1, OF undefined.
    For signed, if OF=1, then overflow occurred.

## Slide 71: Conditional Move Example
Rewrite the absdiff example using conditional moves instead of conditional branching
absdiff: # x in %edi, y in %esi
movl %edi, %eax # eax = x
movl %esi, %edx # edx = y
subl %esi, %eax # eax = x-y
subl %edi, %edx # edx = y-x
cmpl %esi, %edi # x<y?
cmovl %edx, %eax # eax=edx if <=
ret
int absdiff(
int x, int y)
{
int result;
if (x > y) {
result = x-y;
} else {
result = y-x;
}
return result;
}
Note how the control flow is much easier to predict than all the jumping around with labels, e.g. jle, in the conditionally branched version of absdiff
Notes: The register eax is used to store the return value. In this example, it is set first to x-y. Conditionally, the cmovl instruction will *reset* eax to edx=y-x if x<y. If however x>=y, then nothing happens, i.e. cmov doesn’t change the contents of eax, and the correct value is returned in eax.

## Slide 72: Conditional Move Example
int absdiff(
int x, int y)
{
int result;
if (x > y) {
result = x-y;
} else {
result = y-x;
}
return result;
}
int cmovdiff(int x, int y)
{
int rval = x-y;
int tval = y-x;
int test = x < y;
if (test) rval = tval;
return rval;
}

## Slide 73: Conditional Move Example
absdiff: # x in %edi, y in %esi
movl %edi, %eax # eax = x
movl %esi, %edx # edx = y
subl %esi, %eax # eax = x-y
subl %edi, %edx # edx = y-x
cmpl %esi, %edi # x<y?
cmovl %edx, %eax # eax=edx if <=
ret
int cmovdiff(int x, int y)
{
int rval = x-y;
int tval = y-x;
int test = x < y;
if (test) rval = tval;
return rval;
}

## Slide 74: Conditional Move Example
absdiff: # x in %edi, y in %esi
movl %edi, %eax # eax = x
movl %esi, %edx # edx = y
subl %esi, %eax # eax = x-y
subl %edi, %edx # edx = y-x
cmpl %esi, %edi # x<y?
cmovl %edx, %eax # eax=edx if <=
ret
int cmovdiff(int x, int y)
{
int rval = x-y;
int tval = y-x;
int test = x < y;
if (test) rval = tval;
return rval;
}

## Slide 75: Conditional Move Example
absdiff: # x in %edi, y in %esi
movl %edi, %eax # eax = x
movl %esi, %edx # edx = y
subl %esi, %eax # eax = x-y
subl %edi, %edx # edx = y-x
cmpl %esi, %edi # x<y?
cmovl %edx, %eax # eax=edx if <=
ret
int cmovdiff(int x, int y)
{
int rval = x-y;
int tval = y-x;
int test = x < y;
if (test) rval = tval;
return rval;
}

## Slide 76: Conditional Move Example
Control flow is more predictable, but both branches must be evaluated
absdiff: # x in %edi, y in %esi
movl %edi, %eax # eax = x
movl %esi, %edx # edx = y
subl %esi, %eax # eax = x-y
subl %edi, %edx # edx = y-x
cmpl %esi, %edi # x<y?
cmovl %edx, %eax # eax=edx if <=
ret
int cmovdiff(int x, int y)
{
int rval = x-y;
int tval = y-x;
int test = x < y;
if (test) rval = tval;
return rval;
}

## Slide 77: General Form with Conditional Move
C Code
Conditional Move Version
val1 = Then-Expr;
val2 = Else-Expr;
val1 = val2 if !Test;
Both values get computed
Overwrite then-value with else-value if condition doesn’t hold
Don’t use when:
  Then or else expression have side effects, like dereferencing a null pointer or incrementing a global variable (then & else expressions always evaluated)
  Then and else expressions are too expensive
val = Test ? Then-Expr : Else-Expr;

## Slide 78: Jump-to-Middle “While” Loop Translation
Goto Version #3
int fact_while_goto3(int x)
{
int result = 1;
goto middle;
loop:
result *= x;
x = x-1;
middle:
if (x > 1)
goto loop;
return result;
}
Recent technique for GCC
  Both IA32 & x86-64
First iteration jumps over body computation within loop
Goto Version #2
int fact_while_goto2(int x)
{
int result = 1;
if (!(x > 1))
goto done;
loop:
result *= x;
x = x-1;
if (x > 1)
goto loop;
done:
return result;
}

## Slide 79: Jump-to-Middle While Loop Translation
C Code
while (Test)
Body
Avoids duplicating test code
Unconditional goto incurs no performance penalty
for loops compiled in similar fashion
Goto Version
goto middle;
loop:
Body
middle:
if (Test)
goto loop;
Goto (Previous) Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 80: Jump-to-Middle Assembly Example
# x in %edx, result in %eax
jmp .L34 # goto Middle
.L35: # Loop:
imull %edx, %eax # result *= x
decl %edx # x--
.L34: # Middle:
cmpl $1, %edx # x:1
jg .L35 # if >, goto Loop
Goto Version #3
int fact_while_goto3(int x)
{
int result = 1;
goto middle;
loop:
result *= x;
x = x-1;
middle:
if (x > 1)
goto loop;
return result;
}

## Slide 81: Implementing Loops
IA32
  All loops translated into form based on “do-while”
x86-64
  Also make use of “jump to middle”
Why the difference
  IA32 compiler developed for machine where all operations costly
  x86-64 compiler developed for machine where unconditional branches incur (almost) no overhead

## Slide 82: “For” Loop Example
Problems
  For large p, this loop executes p times
    Partial product is multiplied by x each time
  Can we do better?
    Partial product is multiplied by itself each time (squared) until just < xp, then deal with remaining powers
    Executes for loop many fewer times for large p, i.e. O(log(p)) !
/* Compute x raised to nonnegative power p */
int ipwr_for(int x, int p) {
int result=1, i;
for (i=0; i<p; i++) {
result *= x;
}
return result;
}
Compute xp, where x is a positive integer and p is a non-negative integer
  Could build a for loop:
Notes: Want to calculate x^p. Could implement as a for loop that multiplies a partial product times x each time. But for large p, that would execute the for loop p times. Instead, is there a shortcut that executes the for loop fewer times, but still computes the right value x^p? Yes, multiply the partial product not times x, but times itself! That squares the partial product. Keep squaring the partial product until you can no longer square the partial product without exceeding x^p. Multiply by the remaining amount x^p/(squares of partial product x^(2^s)), where s=# times you squared the partial product.

## Slide 83: Faster “For” Loop Example
Example
318 = 32 * 316
= 32 * (((32) 2) 2) 2
  Multiply partial product times itself each time through the loop, which is equivalent to squaring
  In this example, only have to square 4 times, but also have to cleanup remaining powers

## Slide 84: Faster “For” Loop Example
Algorithm
  Exploit property that p = p0 + 2p1 + 4p2 + … 2n–1pn–1
  Gives: xp = z0 · z1 2 · (z2 2) 2 · … · (…((zn –12) 2 )…) 2
    zi = 1 when pi = 0
    zi = x when pi = 1
  Complexity O(log p)
/* Compute x raised to nonnegative power p */
int ipwr_for_fast(int x, unsigned p) {
int result;
for (result = 1; p != 0; p = p>>1) {
if (p & 0x1)
result *= x;
x = x*x;
}
return result;
}
n–1 times

## Slide 85: Switch Statements
Implementation Options
  Series of conditionals, e.g. if- else if - else if -else if…
    Good if few cases
    Slow if many cases, e.g. many compares and conditional jumps
  Jump Table (array of addresses)
    Index into array and jump to branch target
    Avoids conditionals
    Good when cases are small integer constants
  GCC picks one based on case structure
typedef enum
{ADD, MULT, MINUS, DIV, MOD, BAD}
op_type;
char unparse_symbol(op_type op)
{
switch (op) {
case ADD :
return '+';
case MULT:
return '*';
case MINUS:
return '-';
case DIV:
return '/';
case MOD:
return '%';
case BAD:
return '?';
}
}
switch() is missing default case
Notes: typedef int points;
typedef struct MyStruct newtype;
typedef enum {…} op_type; -- means you’re defining op_type as type enum, where the {…} defines the values of the enum
C allows:
enum cardsuit { CLUBS = 1, DIAMONDS = 2, HEARTS = 4, SPADES = 8 };

## Slide 86: Jump Table Structure
switch(op) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
target = JTab[op];
goto *target;
Approx. Translation
Targ0
Targ1
Targ2
Targn-1
•
•
•
JTab:
Jump Table
Note: no conditional evaluation needed, so
very fast to jump to code block, but at cost of
a potentially large jump table
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Jump
Targets
Main Memory

## Slide 87: Switch Statement Example
Branching Possibilities
Setup:
unparse_symbol:
pushl %ebp # Setup
movl %esp,%ebp # Setup
movl 8(%ebp),%eax # eax = op
cmpl $5,%eax # Compare op : 5
ja .L49 # If > goto done
jmp *.L57(,%eax,4) # goto Table[op]
Enumerated Values
  ADD 0
  MULT 1
  MINUS 2
  DIV 3
  MOD 4
  BAD 5
typedef enum
{ADD, MULT, MINUS, DIV, MOD, BAD}
op_type;
char unparse_symbol(op_type op)
{
switch (op) {
• • •
}
}

## Slide 88: Assembly Setup Explanation
  jmp *.L57(,%eax,4)
  Start of jump table denoted by label .L57
  Register %eax holds op
  Must scale by factor of 4 to get offset into table, as each address in jump table is 4 bytes wide (on a 32-bit system)
  Fetch target from effective Address .L57 + op*4
Table Structure
  Array of target memory addresses, so each target requires 4 bytes
  Base address at .L57
Symbolic Labels
  jmp .L49
  Jump target is denoted by label .L49
  Labels of form .LXX translated into addresses (absolute or PC-relative) by assembler

## Slide 89: Jump Table
Enumerated Values
  ADD 0
  MULT 1
  MINUS 2
  DIV 3
  MOD 4
  BAD 5
.section .rodata
.align 4
.L57:
.long .L51 #Op = 0
.long .L52 #Op = 1
.long .L53 #Op = 2
.long .L54 #Op = 3
.long .L55 #Op = 4
.long .L56 #Op = 5
Table Contents
.L51:
movl $43,%eax # ’+’
jmp .L49
.L52:
movl $42,%eax # ’*’
jmp .L49
.L53:
movl $45,%eax # ’-’
jmp .L49
.L54:
movl $47,%eax # ’/’
jmp .L49
.L55:
movl $37,%eax # ’%’
jmp .L49
.L56:
movl $63,%eax # ’?’
# Fall Through to .L49
Targets & Completion

## Slide 90: Switch Statement Completion
Puzzle
  What value returned when op is invalid?
Answer
  Register %eax set to op at beginning of procedure
  This becomes the returned value
Advantage of Jump Table
  Can do k-way branch in O(1) operations
.L49: # Done:
movl %ebp,%esp # Finish
popl %ebp # Finish
ret # Finish

## Slide 91: Switch Object Code
Setup
  Label .L49 becomes address 0x804875c
  Label .L57 becomes address 0x8048bc0
08048718 <unparse_symbol>:
8048718: 55 pushl %ebp
8048719: 89 e5 movl %esp,%ebp
804871b: 8b 45 08 movl 0x8(%ebp),%eax
804871e: 83 f8 05 cmpl $0x5,%eax
8048721: 77 39 ja 804875c <unparse_symbol+0x44>
8048723: ff 24 85 c0 8b jmp *0x8048bc0(,%eax,4)

## Slide 92: Switch Object Code (cont.)
Jump Table
  Doesn’t show up in disassembled code
  Can inspect using GDB
  gdb code-examples
  (gdb) x/6xw 0x8048bc0
    Examine 6 hexadecimal format “words” (4-bytes each)
    Use command “help x” to get format documentation
  0x8048bc0 <_fini+32>:
  0x08048730
  0x08048737
  0x08048740
  0x08048747
  0x08048750
  0x08048757
These are memory address pointers/jump
targets to the code blocks for the different
cases of the switch() statement

## Slide 93: Extracting Jump Table from Binary
Jump Table Stored in Read Only Data Segment (.rodata)
  Various fixed values needed by your code
Can examine with objdump
  objdump code-examples –s –-section=.rodata
  Show everything in indicated segment.
Hard to read
  Jump table entries shown with reversed byte ordering
  E.g., 30870408 really means 0x08048730
Contents of section .rodata:
8048bc0 30870408 37870408 40870408 47870408 0...7...@...G...
8048bd0 50870408 57870408 46616374 28256429 P...W...Fact(%d)
8048be0 203d2025 6c640a00 43686172 203d2025 = %ld..Char = %
…

## Slide 94: Disassembled Targets
  movl %esi,%esi does nothing
  Inserted to align instructions for better cache performance
8048730: b8 2b 00 00 00 movl $0x2b,%eax #‘+’
8048735: eb 25 jmp 804875c <unparse_symbol+0x44>
8048737: b8 2a 00 00 00 movl $0x2a,%eax #‘*’
804873c: eb 1e jmp 804875c <unparse_symbol+0x44>
804873e: 89 f6 movl %esi,%esi
8048740: b8 2d 00 00 00 movl $0x2d,%eax #‘-’
8048745: eb 15 jmp 804875c <unparse_symbol+0x44>
8048747: b8 2f 00 00 00 movl $0x2f,%eax #’/’
804874c: eb 0e jmp 804875c <unparse_symbol+0x44>
804874e: 89 f6 movl %esi,%esi
8048750: b8 25 00 00 00 movl $0x25,%eax #’%’
8048755: eb 05 jmp 804875c <unparse_symbol+0x44>
8048757: b8 3f 00 00 00 movl $0x3f,%eax #’?’

## Slide 95: Matching Disassembled Targets
8048730: b8 2b 00 00 00 movl
8048735: eb 25 jmp
8048737: b8 2a 00 00 00 movl
804873c: eb 1e jmp
804873e: 89 f6 movl
8048740: b8 2d 00 00 00 movl
8048745: eb 15 jmp
8048747: b8 2f 00 00 00 movl
804874c: eb 0e jmp
804874e: 89 f6 movl
8048750: b8 25 00 00 00 movl
8048755: eb 05 jmp
8048757: b8 3f 00 00 00 movl
Jump Table
Entry
0x08048730
0x08048737
0x08048740
0x08048747
0x08048750
0x08048757
Target Code Block of Case in Switch()

## Slide 96: Sparse Switch Example
  Not practical to use jump table
    Would require 10000 entries
  Obvious translation into if-then-else would have maximum of 9 tests in the worst case
    Can we do better?
/* Return x/1111 if x is multiple
&& <= 9999. -1 otherwise */
int div1111(int x)
{
switch(x) {
case 0: return 0;
case 1111: return 1;
case 2222: return 2;
case 3333: return 3;
case 4444: return 4;
case 5555: return 5;
case 6666: return 6;
case 7777: return 7;
case 8888: return 8;
case 9999: return 9;
default: return -1;
}
}

## Slide 97: Sparse Switch Code Structure
  Organizes the cases as a binary tree
  Logarithmic performance, i.e. order O(logN) in complexity
    Worst case of 4 compares vs. ~9 for linear search of cases
-1
-1
-1
-1
4444
1111
7777
0
2222
5555
8888
3333
6666
9999
0
1
4
7
5
8
9
2
3
6
<

=
>
=
<
>
=
<
>
=
<
>
=

=

=

=

=

=

## Slide 98: Sparse Switch Code
  Compares x to possible case values
  Jumps different places depending on outcomes
movl 8(%ebp),%eax # get x
cmpl $4444,%eax # x:4444
je L8
jg L16
cmpl $1111,%eax # x:1111
je L5
jg L17
testl %eax,%eax # x:0
je L4
jmp L14
. . .
. . .
L5:
movl $1,%eax
jmp L19
L6:
movl $2,%eax
jmp L19
L7:
movl $3,%eax
jmp L19
L8:
movl $4,%eax
jmp L19
. . .

## Slide 99: C operators – Assembly Equivalents?
Operators Associativity
() [] -> . left to right
! ~ ++ -- + - * & (type) sizeof right to left
* / % left to right
+ - left to right
<< >> left to right
< <= > >= left to right
== != left to right
& left to right
^ left to right
| left to right
&& left to right
|| left to right
?: right to left
= += -= *= /= %= &= ^= != <<= >>= right to left
, left to right
Note: Unary +, -, and * have higher precedence than binary forms