## Slide 1: Chapter 4: Processor Architecture
Topics:
  Y86 Instruction Set Architecture
  Pipelining to improve performance
  Data Hazards
  Branch Misprediction

## Slide 2: Announcements
Midterm #2 results
  Average = 54
  Final grades incorporate course difficulty but exams not curved
  Solutions released after late test takers finish exam this week
  If you need a regrade, drop by Prof. Han’s office hours

## Slide 3: Announcements
Attack Lab #3 due Monday Oct 30 at 9 am
  Sign up for grading time slots later this week
Next recitation exercise released later this week
Read:
  Chapter 4.1, 4.3.1-4.3.2, “Surveying SEQ” in 4.3.3, 4.4, 4.5.1-4.5.6
  Do Practice problems
Upcoming schedule:
  Mon Nov 13 Lab #4 due (released next week)
  Wed Nov 15 Midterm #3

## Slide 4: Major Revelations So Far…
Two’s complement encoding and arithmetic for integers
Programs in high-level languages are compiled into assembly instructions and executed on the CPU
Assembly uses a call stack to efficiently manage function calls
Call stacks can be overflowed on x86 CPUs, resulting in execution of malicious code
Floating point representation encodes real #s as M*2E, and x86 has separate FP registers & instructions
Next up: How to improve performance using 1) pipelining, 2) parallelism, and 3) caching

## Slide 5: Binary Object Code
00401040 <_sum>:
0: 55 push %ebp
1: 89 e5 mov %esp,%ebp
3: 8b 45 0c mov 0xc(%ebp),%eax
6: 03 45 08 add 0x8(%ebp),%eax
9: 89 ec mov %ebp,%esp
b: 5d pop %ebp
c: c3 ret
d: 8d 76 00 lea 0x0(%esi),%esi
Encoding & Execution
  How is it that “55” represents “push %ebp”
  How is it that “03 45 08” represents “add 0x8(%ebp), %eax”?
  Note how the encodings are variable length
  How does the CPU execute each instruction?
Notes: Disassembled object code

## Slide 6: Y86 Processor State
%r8
%r9
%r10
%r11
%r12
%r13
%r14
  Program Registers
    15 similar to x86-64. Each 64 bits
  Condition Codes
    Single-bit flags set by arithmetic or logical instructions
      OF: Overflow ZF: Zero SF:Negative
  Program Counter
    Indicates address of instruction
  Memory
    Byte-addressable storage array
    Words stored in little-endian byte order
Program registers
Condition codes
PC
Memory
OF
ZF
SF
%rax
%rcx
%rdx
%rbx
%rsp
%rbp
%rsi
%rdi

## Slide 7: Y86 Instructions
Format
  1--10 bytes of information read from memory
    Can determine instruction length from first byte
    Not as many instruction types, and simpler encoding than with x86-64
  Each accesses and modifies some part(s) of the program state

## Slide 8: Encoding Registers
Each register has 4-bit ID
  Same encoding as in x86-64
Register ID 15 indicates “no register”
  Will use this in our hardware design in multiple places
%rax
%rcx
%rdx
%rbx
%rsp
%rbp
%rsi
%rdi
0
1
2
3
4
5
6
7
%r8
%r9
%r10
%r11
%r12
%r13
%r14
8
9
A
B
C
D
E
F

## Slide 9: Instruction Example
  Add value in register rA to that in register rB
    Store result in register rB
    Note that Y86 only allows addition to be applied to register data
  Two-byte encoding
    First indicates instruction type
    Second gives source and destination registers
  e.g., addq %rax,%rsi Encoding: 60 06
  Set condition codes based on result
addq rA, rB
6
0
rA
rB
Encoded Representation
Generic Form
Addition Instruction

## Slide 10: Arithmetic and Logical Operations
  Refer to generically as “OPq”
  Encodings differ only by “function code”
    Low-order 4 bits in first instruction word
  Operate only on register data, not memory
    Unlike x86-64, where one of operands could be a memory location
    Separate move instructions to operate on memory
  Set condition codes as side effect
addq rA, rB
6
0
rA
rB
subq rA, rB
6
1
rA
rB
andq rA, rB
6
2
rA
rB
xorq rA, rB
6
3
rA
rB
Add
Subtract (rA from rB)
And
Exclusive-Or
Instruction Code
Function Code

## Slide 11: Move Operations
  Like the x86 movq instruction
  Simpler format for memory addresses
  Give different names to keep them distinct
  Supports only simple addressing mode: D(rX)
rrmovq rA, rB
2
0
rA
rB
Register --> Register
Immediate --> Register
irmovq V, rB
3
0
f
rB
V
Register --> Memory
rmmovq rA, D(rB)
4
0
rA
rB
D
Memory --> Register
mrmovq D(rB), rA
5
0
rA
rB
D
Notes: Note in mrmovq how the order of rA and rB are reversed in the encoding.

## Slide 12: Jump Instructions
  Refer to generically as “jXX”
  Encodings differ only by “function code”
  Based on values of condition codes
  Same as x86-64 counterparts
  Encode full destination address
    Unlike PC-relative addressing seen in x86
jmp Dest
7
0
Jump Unconditionally
Dest
jle Dest
7
1
Jump When Less or Equal
Dest
jl Dest
7
2
Jump When Less
Dest
je Dest
7
3
Jump When Equal
Dest
jne Dest
7
4
Jump When Not Equal
Dest
jge Dest
7
5
Jump When Greater or Equal
Dest
jg Dest
7
6
Jump When Greater
Dest

## Slide 13: Y86 Program Stack
  Region of memory holding program data
  Used in Y86 (and x86) for supporting procedure calls
  Stack top indicated by %rsp
    Address of top stack element
  Stack grows toward lower addresses
    Top element is at highest address in the stack
    When pushing, must first decrement stack pointer
    When popping, increment stack pointer
%rsp
•
•
•
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 14: Stack Operations
  Decrement %rsp by 8
  Store word from rA to memory at %rsp
  Like x86-64
  Read word from memory at %rsp
  Save in rA
  Increment %rsp by 8
  Like x86-64
pushq rA
a
0
rA
f
popq rA
b
0
rA
f

## Slide 15: Subroutine Call and Return
  Push address of next instruction onto stack
  Start executing instructions at Dest
  Like x86-64
  Pop value from stack
  Use as address for next instruction
  Like x86-64
call Dest
8
0
Dest
ret
9
0

## Slide 16: Miscellaneous Instructions
  Don’t do anything
  Stop executing instructions
  x86 has comparable instruction, but can’t execute it in user mode
  We will use it to stop the simulator
nop
1
0
halt
0
0

## Slide 17: Y86 Instruction Set
Byte
0
1
2
...
...
9
pushq rA
A
0
rA
f
jXX Dest
7
fn
Dest
popq rA
B
0
rA
f
call Dest
8
0
Dest
rrmovq rA, rB
2
0
rA
rB
irmovq V, rB
3
0
f
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPl rA, rB
6
fn
rA
rB
ret
9
0
halt
0
0
nop
1
0
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6
addq
6
0
subq
6
1
andq
6
2
xorq
6
3

## Slide 18: Writing Y86 Code
Try to Use C Compiler as Much as Possible
  Write code in C and compile for x86-64 with gcc -S
  Transliterate into Y86
  Wrote an assembler called YAS
Coding Example
  Sum count elements in a long array starting at pointer start

## Slide 19: Y86 Code Generation Example
/* Sum count # of longs
starting at ptr “start” */
long sum(long *start, long count)
{
long sum = 0;
while (count) {
sum += *start;
start++;
count--;
}
return sum;
}
C code:
/* start in %rdi, count in %rsi */
sum:
movl %0, %eax // sum = 0
jmp .L2 // goto test
.L3: // loop:
addq (%rdi), %rax // add *start to sum
addq $8, %rdi // start++
subq $1, %rsi // count—
.L2: // test:
testq %rsi, %rsi // test sum
jne .L3 // if !=0, goto loop
rep; ret // return
X86-64 code:

## Slide 20: Y86 Code Generation Example
/* start in %rdi,
count in %rsi */
sum:
movl %0, %eax
jmp .L2
.L3:
addq (%rdi), %rax
addq $8, %rdi
subq $1, %rsi
.L2:
testq %rsi, %rsi
jne .L3
rep; ret
X86-64 code:
/* start in %rdi,
count in %rsi */
sum:
irmovq $8, %r8 // constant 8
irmovq $1, %r9 // constant 1
xorq %rax %rax // sum = 0
andq %rsi,%rsi // set CC
jmp test // goto test
loop : // loop:
mrmovq (%rdi), %r10 // get *start
addq %r10,%rax // add to sum
addq %r8, %rdi // start++
subq $r9, %rsi // count—, set CC
test: // test:
jne loop // stop when 0
ret // return
Y86-64 code:

## Slide 21: Executing CPU Instructions
Each Y86 instruction can be divided into 6 stages of execution, e.g. addq %rdx,%rcx and mrmovq 4(%rdx), %rcx
  Fetch instruction
  Decode Instruction
  Execute Instruction
  Store results to memory or retrieve values from memory
  Write back results to registers
  Update CPU state
    Update PC
  This is the SEQ architecture of the textbook

## Slide 22: Instruction Decoding
Instruction Format – Different Fields
  Instruction byte icode:ifun
  Optional register byte rA:rB
  Optional constant word valC
6
0
rA
rB
D
icode
ifun
rA
rB
valC
Optional
Optional
Notes: add has register byte but not constant word
j* has constant word but not register byte
mrmov and rmmove have both

## Slide 23: Arithmetic Logic Unit
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
  Combinational logic
    Continuously responding to inputs
  Control signal selects function computed
    Corresponding to 4 arithmetic/logical operations in Y86
  Also computes values for condition codes
A
L
U
Y
X
X + Y
Function code = 0
A
L
U
Y
X
X - Y
Function code = 1
A
L
U
Y
X
X & Y
Function code = 2
A
L
U
Y
X
X ^ Y
Function code = 3
A
B
A
B
A
B
A
B

## Slide 24: SEQ Hardware
Some lines
omitted for
brevity
Notes: Note: not every line/connection is shown. Some are omitted for brevity.
valP is input as Data to memory stage since a call will push the return address (= valP) into memory on the stack

## Slide 25: Executing An Arithmetic/Logical Operation
Fetch
  Read 2 bytes
Decode
  Read operand registers
Execute
  Perform operation
  Set condition codes
Memory
  Do nothing
Write back
  Update register
PC Update
  Increment PC by 2
OPq rA, rB
6
fn
rA
rB

## Slide 26: Stage Computation: Arith/Log. Ops
  Formulate instruction execution as sequence of simple steps
  Use same general form for all instructions
OPq rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB OP valA
Set CC
Execute
Perform ALU operation
Set condition code register
Memory
R[rB]  valE
Write
back
Write back result
PC  valP
PC update
Update PC

## Slide 27: Execution Example
addq %rdx, %rcx
  Encoding: 0x6021
  Byte 1
    icode=6
    ifun=0
  Byte 2
    rA=%rdx=2
    rB=%rcx=1
1. Fetch instruction
= 0x6021 from
mem loc pointed to by PC
2. Decode values
6 0 2 1
%rdx
%rcx
3. ALU executes addq
instruction on inputs,
generates result
addq
4. Result is written
back to %rcx.
%rdx+
%rcx
5. Memory stage is
unused for Y86 addq

## Slide 28: Executing rmmovq
Fetch
  Read 10 bytes
Decode
  Read operand registers
Execute
  Compute effective address
Memory
  Write to memory
Write back
  Do nothing
PC Update
  Increment PC by 10
rmmovq rA, D(rB)
4
0
rA
rB
D

## Slide 29: Stage Computation: rmmovq
  Use ALU for address computation
rmmovq rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB + valC
Execute
Compute effective address
M8[valE]  valA
Memory
Write value to memory
Write
back
PC  valP
PC update
Update PC

## Slide 30: rmmovq Execution
Example:
rmmovq %rdx, 8(%rcx)
  Encoding: 0x40210800000000000000
  Byte 1
    icode=4
    ifun=0
  Byte 2
    rA=%rdx=2
    rB=%rcx=1
  Bytes 3-10
    valC = 8 = Displacement D
    D = 0x0800000000000000 (is stored in byte-reversed little Endian order )
1. Fetch instruction
= 0x40210800000000000000
from mem loc pointed to by PC
5. No writeback
stage for rmmovq
3. ALU executes rmmovq
by adding to compute
an effective address
8
%rcx
add
addresses
%rcx+
8
4. %rdx is written
in memory location
%rcx+8
%rdx
Store
2. Decode values
4 0 2 1
0x08

## Slide 31: Executing popq
Fetch
  Read 2 bytes
Decode
  Read stack pointer
Execute
  Increment stack pointer by 8
Memory
  Read from old stack pointer
Write back
  Update stack pointer
  Write result to register
PC Update
  Increment PC by 2
popq rA
b
0
rA
f
  Normally you first pop into a register, then shrink the stack pointer, but here we reverse the order due to the hardware stage design
    Have to remember both old and new stack pointer values
Notes: Note how unlike the previous two examples of addq and rmmovq, popq requires both the memory stage and write-back stage to be busy in order to successfully complete the instruction.

## Slide 32: Stage Computation: popq
  Use ALU to increment stack pointer
  Must update two registers
    Popped value
    New stack pointer
popq rA
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[%rsp]
valB  R [%rsp]
Decode
Read stack pointer
Read stack pointer
valE  valB + 8
Execute
Increment stack pointer
valM  M8[valA]
Memory
Read from stack
R[%rsp]  valE
R[rA]  valM
Write
back
Update stack pointer
Write back result
PC  valP
PC update
Update PC

## Slide 33: Executing Jumps
Fetch
  Read 9 bytes
  Increment PC by 9
Decode
  Do nothing
Execute
  Determine whether to take branch based on jump condition and condition codes
Memory
  Do nothing
Write back
  Do nothing
PC Update
  Set PC to Dest if branch taken or to incremented PC if not branch
jXX Dest
7
fn
Dest
XX
XX
fall thru:
XX
XX
target:
Not taken
Taken

## Slide 34: Stage Computation: Jumps
  Compute both addresses
  Choose based on setting of condition codes and branch condition
jXX Dest
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
Fetch
Read instruction byte
Read destination address
Fall through address
Decode
Cnd  Cond(CC,ifun)
Execute
Take branch?
Memory
Write
back
PC  Cnd ? valC : valP
PC update
Update PC

## Slide 35: Pipelining
Executing a single instruction at a time leaves many stages idle
What happens if we insert a bank of registers between each stage?
  The result of each stage can be saved
  As instruction I reaches the Writeback stage, all previous stages are busy
    Memory stage occupied by instructions I+1
    Execute stage occupied by instruction I+2
    Decode stage occupied by instruction I+3
    Fetch stage occupied by instruction I+4, .etc…
Pipeline Example:
addq
subq
movq
cmpq
jle

## Slide 36: Pipelining
End result is faster rate of execution thanks to pipelining
  Previous non-pipelined rate = one instruction per all six stages
  New pipelined rate = one instruction per a single stage, i.e. interarrival time between instructions at output of pipeline is one stage
  New pipelined rate >> previous non-pipelined rate
  However, the cumulative delay of each individual instruction through the full CPU (all stages) is still approximately the same
Pipeline Example:
addq
subq
movq
cmpq
jle

## Slide 37: Real-World Pipelines: Car Washes
Idea
  Divide process into independent stages
  Move objects through stages in sequence
  At any given time, multiple objects being processed
Sequential
Parallel
Pipelined

## Slide 38: Computational Example
System
  Register stores or latches the results of the combinational logic on the rising edge of the clock
  Computation requires total of 300 picoseconds
  Additional 20 picoseconds to save result in register
  Must have clock cycle of at least 320 ps
  If combinational logic represents a CPU processing an instruction, then throughput = 1/320 ps = 3.12 GOPS
Combinational
logic
R
e
g
300 ps
20 ps
Clock
Delay = 320 ps
Throughput = 3.12 GOPS

## Slide 39: 3-Way Pipelined Version
System
  Divide combinational logic into 3 blocks of 100 ps each
  Can begin new operation as soon as previous one passes through stage A.
    Begin new operation every 120 ps
    Throughput = 1/120 ps = 8.33 GOPS  2.67 times faster throughput!
  Overall latency increases
    360 ps from start to finish
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Delay = 360 ps
Throughput = 8.33 GOPS

## Slide 40: Pipeline Diagrams
Unpipelined
  Cannot start new operation until previous one completes
3-Way Pipelined
  Up to 3 operations in process simultaneously
Time
OP1
OP2
OP3
Time
A
B
C
A
B
C
A
B
C
OP1
OP2
OP3

## Slide 41: Operating a Pipeline
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C
0
120
240
360
480
640
Clock
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
239
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
241
R
e
g
R
e
g
R
e
g
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Comb.
logic
A
Comb.
logic
B
Comb.
logic
C
Clock
300
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
359

## Slide 42: Limitations: Nonuniform Delays
  Throughput limited by slowest stage
  Other stages sit idle for much of the time
  Challenging to partition system into balanced stages
R
e
g
Clock
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
50 ps
20 ps
150 ps
20 ps
100 ps
20 ps
Delay = 510 ps
Throughput = 5.88 GOPS
Comb.
logic
A
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C

## Slide 43: Limitations: Register Overhead
  As we try to deepen the pipeline, the overhead of loading registers becomes more significant
  Percentage of clock cycle spent loading register:
    1-stage pipeline: 6.25%
    3-stage pipeline: 16.67%
    6-stage pipeline: 28.57%
  High speeds of modern processor designs obtained through very deep pipelining (15 or more stages)
Delay = 420 ps, Throughput = 14.29 GOPS
Clock
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps

## Slide 44: Data Dependencies
System
  Each operation depends on result from preceding one
Clock
Combinational
logic
R
e
g
Time
OP1
OP2
OP3

## Slide 45: Data Hazards
  Result does not feed back around in time for next operation
  Pipelining has changed behavior of system
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C
OP4
A
B
C

## Slide 46: Data Dependencies in Processors
  Result from one instruction used as operand for another
    Read-after-write (RAW) dependency
  Very common in actual programs
  Must make sure our pipeline handles these properly
    Get correct results
    Minimize performance impact
1 irmovq $50, %rax
2 addq %rax , %rbx
3 mrmovq 100( %rbx ), %rdx

## Slide 47: Adding Pipeline Registers
Add pipeline registers between each stage
  W registers are between the Memory and Writeback stages
  M registers are between the Execute and Memory stages
  E registers are between the Decode and Execute stages
  D registers are between Fetch and Decode stages
  F registers are for storing the predicted next instruction of the program counter PC
    Reorganize Y86 CPU to do PC prediction in the first stage rather than the last stage - see textbook
W
M
E
D
F
Notes: This is effectively the PIPE- implementation in the textbook Figure 4.41

## Slide 48: Predicting the PC
  Start fetch of new instruction after current one has completed fetch stage
    Not enough time to reliably determine next instruction
  Guess which instruction will follow
    Recover if prediction was incorrect

## Slide 49: Our PC Prediction Strategy
Instructions that Don’t Transfer Control
  Examples: sequence of instructions like addl followed by irmovl followed by andl followed by …
  Predict next PC to be valP
  Always reliable
Call and Unconditional Jumps:
  e.g. call/jmp 0xffff0a42
  Predict next PC to be valC (destination)
  Always reliable

## Slide 50: Our PC Prediction Strategy
Conditional Jumps:
  e.g. jle 0xffff0a42
  Where to jump next depends on results of condition codes of the previous instruction, which has still not even reached the Execute stage where the condition codes are generated!
  Branch prediction strategy: Predict next PC to be the jump address/destination (valC)
    So Y86 default is to always take the branch – always taken branch prediction strategy
    Typically right 60% of time
  Begin speculative execution - Only correct if branch is taken
    If incorrect, must flush pipeline and discard speculative execution results
Notes: “A slightly more sophisticated strategy, known as backward taken, forward not-taken (BTFNT), predicts
that branches to lower addresses than the next instruction will be taken, while those to higher addresses
will not be taken. This strategy has a success rate of around 65%. This improvement stems from the fact
that loops are closed by backward branches, and loops are generally executed multiple times. Forward
branches are used for conditional operations, and these are less likely to be taken.” – p. 428
“As we saw in Section 3.6.6, mispredicted branches can degrade the performance of a program
considerably, thus motivating the use of conditional data transfer rather than conditional control
transfer when possible” – p. 428

## Slide 51: Our PC Prediction Strategy
Return Instruction: ret
  Where to jump next depends on popping the return address off the stack, which means pulling it from memory – an operation that occurs many stages in the future!
  Don’t try to predict

## Slide 52: Recovering from PC Misprediction
  Mispredicted Jump
    Will see branch flag once instruction reaches memory stage
    Can get fall-through PC from valP
    Have to flush/ignore much of pipeline, fetch correct instruction and start to fill pipeline again
  Return Instruction
    Will get return PC when ret reaches write-back stage
    Pipeline goes mostly empty

## Slide 53: Pipeline Demonstration

## Slide 54: Data Dependencies: No Nop
Assume all registers initialized to zero

## Slide 55: Data Dependencies: 3 Nop’s
Notes: The CPU hardware can dynamically detect a data dependency, as in the add instruction here, and *stall* the forward progress of that instruction through the pipeline until the results are ready. In this case, the add would be stalled at the decode stage waiting until both %rdx and %rax were set properly/written back. This stalling effectively introduces nops into the pipeline without needing a compiler to do it.

## Slide 56: Stalling an Instruction
CPU hardware recognizes a data dependency/hazard and stalls an instruction until results are ready
  In our example, addq instruction depends on %rdx and %rax
  These are not set until the Writeback stages of each irmovq are done
  So stall addq instruction at the Decode stage, introducing bubbles or effectively nops

## Slide 57: Branch Misprediction Example
  Should only execute first 7 instructions
0x000: xorl %eax,%eax # %eax always zero
0x002: jne t # Not taken
0x007: irmovl $1, %eax # Fall through
0x00d: nop
0x00e: nop
0x00f: nop
0x010: halt
0x011: t: irmovl $3, %edx # Target (Should not execute)
0x017: irmovl $4, %ecx # Should not execute
0x01d: irmovl $5, %edx # Should not execute

## Slide 58: Branch Misprediction Trace
  Incorrectly execute multiple instructions at branch target
  CPU hardware realizes a mistake has occurred in branch prediction, and ignores the results of speculative execution, makes the correct jump and starts refilling the pipeline
Notes: It’s not until the M stage that the M registers receives the condition codes from the E stage, and can feedback to the PC predictor that a branch has been mispredicted. See full PIPE diagram p. 440 Fig 4.52.

## Slide 59: Return Example
0x000: irmovl Stack,%esp # Initialize stack pointer
0x006: nop # Avoid hazard on %esp
0x007: nop
0x008: nop
0x009: call p # Procedure call
0x00e: irmovl $5,%esi # Return point
0x014: halt
0x020: .pos 0x20
0x020: p: nop # procedure
0x021: nop
0x022: nop
0x023: ret
0x024: irmovl $1,%eax # Should not be executed
0x02a: irmovl $2,%ecx # Should not be executed
0x030: irmovl $3,%edx # Should not be executed
0x036: irmovl $4,%ebx # Should not be executed
0x100: .pos 0x100
0x100: Stack: # Stack: Stack pointer
  Require lots of nops to avoid data hazards
Notes: Note the 3 nops in p are to avoid a 2nd data hazard between call p and ret, namely call p will change the stack pointer, which takes time to flow through the pipeline until the Writeback stage. There are 3 nops because when the call p is at the Writeback stage, the ret can be at the Decode stage, which is a difference of 3 stages.

## Slide 60: Incorrect Return Example
  Incorrectly execute 3 instructions following ret

## Slide 61: Chapter Mapping
Lines of
Source
code
Lines of
Assembly
code
Lines of
Binary
code &
data
10101010
00001010
01010111
Memory
11101110
00111011
10000111
10101010
add a,b
sub a,b
move a…
Chapter 3
Chapters 3, 4, 5 and 6
Chapter 7
Chapter 9
Chapter 5
Chapter 2
Pre-processor
&
Compiler
Assembler
&
Linker
Operating
System
Chapter 8

## Slide 62: Supplementary Slides Chapter 4

## Slide 63: Instruction Set Architecture
Assembly Language View
  Processor state
    Registers, memory, …
  Instructions
    addl, movl, leal, …
    How instructions are encoded as bytes
Layer of Abstraction
  Above: how to program machine
    Processor executes instructions in a sequence
  Below: what needs to be built
    Use variety of tricks to make it run fast
    E.g., execute multiple instructions simultaneously
ISA
Compiler
OS
CPU
Design
Circuit
Design
Chip
Layout
Application
Program

## Slide 64: Building Blocks
Combinational Logic
  Compute Boolean functions of inputs
  Continuously respond to input changes
  Operate on data and implement control
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Clock
A
L
U
fun
A
B
MUX
0
1
=
Clock
Storage Elements
  Store bits
  Addressable memories
  Non-addressable registers
    Loaded only as clock rises

## Slide 65: Move Instruction Examples (32-bit)
irmovl $0xabcd, %edx
movl $0xabcd, %edx
30 82 cd ab 00 00
IA32
Y86
Encoding
rrmovl %esp, %ebx
movl %esp, %ebx
20 43
mrmovl -12(%ebp),%ecx
movl -12(%ebp),%ecx
50 15 f4 ff ff ff
—
movl $0xabcd, (%eax)
—
movl %eax, 12(%eax,%edx)
—
movl (%ebp,%eax,4),%ecx
rmmovl %esi,0x41c(%esp)
movl %esi,0x41c(%esp)
40 64 1c 04 00 00

## Slide 66: Y86 Code Generation Example (32-bit)
First Try
  Write typical array code
  Compile with gcc -O2 -S
Problem
  Hard to do array indexing on Y86
    Since don’t have scaled addressing modes
/* Find number of elements in
null-terminated list */
int len1(int a[])
{
int len;
for (len = 0; a[len]; len++)
;
return len;
}
L18:
incl %eax
cmpl $0,(%edx,%eax,4)
jne L18

## Slide 67: Y86 Code Generation Example #2 (32-bit)
Second Try
  Write with pointer code
  Compile with gcc -O2 -S
Result
  Don’t need to do indexed addressing
/* Find number of elements in
null-terminated list */
int len2(int a[])
{
int len = 0;
while (*a++)
len++;
return len;
}
L24:
movl (%edx),%eax
incl %ecx
L26:
addl $4,%edx
testl %eax,%eax
jne L24

## Slide 68: Y86 Code Generation Example #3 (32-bit)
IA32 Code
  Setup
Y86 Code
  Setup
len2:
pushl %ebp
xorl %ecx,%ecx
movl %esp,%ebp
movl 8(%ebp),%edx
movl (%edx),%eax
jmp L26
len2:
pushl %ebp # Save %ebp
xorl %ecx,%ecx # len = 0
rrmovl %esp,%ebp # Set frame
mrmovl 8(%ebp),%edx # Get a
mrmovl (%edx),%eax # Get *a
jmp L26 # Goto entry
L24:
movl (%edx),%eax
incl %ecx
L26:
addl $4,%edx
testl %eax,%eax
jne L24

## Slide 69: Y86 Code Generation Example #4 (32-bit)
IA32 Code
  Loop + Finish
Y86 Code
  Loop + Finish
L24:
movl (%edx),%eax
incl %ecx
L26:
addl $4,%edx
testl %eax,%eax
jne L24
movl %ebp,%esp
movl %ecx,%eax
popl %ebp
ret
L24:
mrmovl (%edx),%eax # Get *a
irmovl $1,%esi
addl %esi,%ecx # len++
L26: # Entry:
irmovl $4,%esi
addl %esi,%edx # a++
andl %eax,%eax # *a == 0?
jne L24 # No—Loop
rrmovl %ebp,%esp # Pop
rrmovl %ecx,%eax # Rtn len
popl %ebp
ret

## Slide 70: Assembling Y86 Program
  Generates “object code” file eg.yo
    Actually looks like disassembler output
  unix> yas eg.ys
  0x000: 308400010000 | irmovl Stack,%esp # Set up stack
  0x006: 2045 | rrmovl %esp,%ebp # Set up frame
  0x008: 308218000000 | irmovl List,%edx
  0x00e: a028 | pushl %edx # Push argument
  0x010: 8028000000 | call len2 # Call Function
  0x015: 10 | halt # Halt
  0x018: | .align 4
  0x018: | List: # List of elements
  0x018: b3130000 | .long 5043
  0x01c: ed170000 | .long 6125
  0x020: e31c0000 | .long 7395
  0x024: 00000000 | .long 0

## Slide 71: Simulating Y86 Program
  Instruction set simulator
    Computes effect of each instruction on processor state
    Prints changes in state from original
  unix> yis eg.yo
  Stopped in 41 steps at PC = 0x16. Exception 'HLT', CC Z=1 S=0 O=0
  Changes to registers:
  %eax: 0x00000000 0x00000003
  %ecx: 0x00000000 0x00000003
  %edx: 0x00000000 0x00000028
  %esp: 0x00000000 0x000000fc
  %ebp: 0x00000000 0x00000100
  %esi: 0x00000000 0x00000004
  Changes to memory:
  0x00f4: 0x00000000 0x00000100
  0x00f8: 0x00000000 0x00000015
  0x00fc: 0x00000000 0x00000018

## Slide 72: Y86 Program Structure
  Program starts at address 0
  Must set up stack
    Make sure don’t overwrite code!
  Must initialize data
  Can use symbolic names
irmovl Stack,%esp # Set up stack
rrmovl %esp,%ebp # Set up frame
irmovl List,%edx
pushl %edx # Push argument
call len2 # Call Function
halt # Halt
.align 4
List: # List of elements
.long 5043
.long 6125
.long 7395
.long 0
# Function
len2:
. . .
# Allocate space for stack
.pos 0x100
Stack:

## Slide 73: Y86 SEQ Hardware Structure
State
  Program counter register (PC)
  Condition code register (CC)
  Register File
  Memories
    Access same memory space
    Data: for reading/writing program data
    Instruction: for reading instructions
Instruction Flow
  Read instruction at address specified by PC
  Process through stages
  Update program counter

## Slide 74: SEQ Stages
Fetch
  Read instruction from instruction memory
Decode
  Read program registers
Execute
  Compute value or address
Memory
  Read or write data
Write Back
  Write program registers
PC
  Update program counter

## Slide 75: SEQ Hardware
Key
  Blue boxes: predesigned hardware blocks
    E.g., memories, ALU
  Gray boxes: control logic
    Describe in HCL
  White ovals: labels for signals
  Thick lines: 32-bit word values
  Thin lines: 4-8 bit values
  Dotted lines: 1-bit values

## Slide 76: Hardware Control Language
  Very simple hardware description language
  Can only express limited aspects of hardware operation
    Parts we want to explore and modify
Data Types
  bool: Boolean
    a, b, c, …
  int: words
    A, B, C, …
    Does not specify word size---bytes, 32-bit words, …
Statements
  bool a = bool-expr ;
  int A = int-expr ;

## Slide 77: HCL Operations
  Classify by type of value returned
Boolean Expressions
  Logic Operations
    a && b, a || b, !a
  Word Comparisons
    A == B, A != B, A < B, A <= B, A >= B, A > B
  Set Membership
    A in { B, C, D }
      Same as A == B || A == C || A == D
Word Expressions
  Case expressions
    [ a : A; b : B; c : C ]
    Evaluate test expressions a, b, c, … in sequence
    Return word expression A, B, C, … for first successful test

## Slide 78: Executing call
Fetch
  Read 5 bytes
  Increment PC by 5
Decode
  Read stack pointer
Execute
  Decrement stack pointer by 4
Memory
  Write incremented PC to new value of stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to Dest
call Dest
8
0
Dest
XX
XX
return:
XX
XX
target:

## Slide 79: Stage Computation: call
  Use ALU to decrement stack pointer
  Store incremented PC
call Dest
icode:ifun  M1[PC]
valC  M4[PC+1]
valP  PC+5
Fetch
Read instruction byte
Read destination address
Compute return point
valB  R[%esp]
Decode
Read stack pointer
valE  valB + –4
Execute
Decrement stack pointer
M4[valE]  valP
Memory
Write return value on stack
R[%esp]  valE
Write
back
Update stack pointer
PC  valC
PC update
Set PC to destination

## Slide 80: Executing ret
Fetch
  Read 1 byte
Decode
  Read stack pointer
Execute
  Increment stack pointer by 4
Memory
  Read return address from old stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to return address
ret
9
0
XX
XX
return:

## Slide 81: Stage Computation: ret
  Use ALU to increment stack pointer
  Read return address from memory
ret
icode:ifun  M1[PC]
Fetch
Read instruction byte
valA  R[%esp]
valB  R[%esp]
Decode
Read operand stack pointer
Read operand stack pointer
valE  valB + 4
Execute
Increment stack pointer
valM  M4[valA]
Memory
Read return address
R[%esp]  valE
Write
back
Update stack pointer
PC  valM
PC update
Set PC to return address

## Slide 82: Computation Steps
  All instructions follow same general pattern
  Differ in what gets computed on each step
OPl rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
[Read constant word]
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB OP valA
Set CC
Execute
Perform ALU operation
Set condition code register
Memory
[Memory read/write]
R[rB]  valE
Write
back
Write back ALU result
[Write back memory result]
PC  valP
PC update
Update PC
icode,ifun
rA,rB
valC
valP
valA, srcA
valB, srcB
valE
Cond code
valM
dstE
dstM
PC

## Slide 83: Computation Steps
  All instructions follow same general pattern
  Differ in what gets computed on each step
call Dest
Fetch
Decode
Execute
Memory
Write
back
PC update
icode,ifun
rA,rB
valC
valP
valA, srcA
valB, srcB
valE
Cond code
valM
dstE
dstM
PC
icode:ifun  M1[PC]
valC  M4[PC+1]
valP  PC+5
valB  R[%esp]
valE  valB + –4
M4[valE]  valP
R[%esp]  valE
PC  valC
Read instruction byte
[Read register byte]
Read constant word
Compute next PC
[Read operand A]
Read operand B
Perform ALU operation
[Set condition code reg.]
[Memory read/write]
[Write back ALU result]
Write back memory result
Update PC

## Slide 84: Computed Values
Fetch
  icode Instruction code
  ifun Instruction function
  rA Instr. Register A
  rB Instr. Register B
  valC Instruction constant
  valP Incremented PC
Decode
  srcA Register ID A
  srcB Register ID B
  dstE Destination Register E
  dstM Destination Register M
  valA Register value A
  valB Register value B
Execute
  valE ALU result
  Bch Branch flag
Memory
  valM Value from memory

## Slide 85: Fetch Logic
Predefined Blocks
  PC: Register containing PC
  Instruction memory: Read 6 bytes (PC to PC+5)
  Split: Divide instruction byte into icode and ifun
  Align: Get fields for rA, rB, and valC

## Slide 86: Fetch Logic
Control Logic
  Instr. Valid: Is this instruction valid?
  Need regids: Does this instruction have a register bytes?
  Need valC: Does this instruction have a constant word?

## Slide 87: Fetch Control Logic
bool need_regids =
icode in { IRRMOVL, IOPL, IPUSHL, IPOPL,
IIRMOVL, IRMMOVL, IMRMOVL };
bool instr_valid = icode in
{ INOP, IHALT, IRRMOVL, IIRMOVL, IRMMOVL, IMRMOVL,
IOPL, IJXX, ICALL, IRET, IPUSHL, IPOPL };

## Slide 88: Decode Logic
Register File
  Read ports A, B
  Write ports E, M
  Addresses are register IDs or 8 (no access)
Control Logic
  srcA, srcB: read port addresses
  dstA, dstB: write port addresses

## Slide 89: A Source
OPl rA, rB
valA  R[rA]
Decode
Read operand A
rmmovl rA, D(rB)
valA  R[rA]
Decode
Read operand A
popl rA
valA  R[%esp]
Decode
Read stack pointer
jXX Dest
Decode
No operand
call Dest
valA  R[%esp]
Decode
Read stack pointer
ret
Decode
No operand
int srcA = [
icode in { IRRMOVL, IRMMOVL, IOPL, IPUSHL } : rA;
icode in { IPOPL, IRET } : RESP;
1 : RNONE; # Don't need register
];

## Slide 90: E Destination
None
R[%esp]  valE
Update stack pointer
None
R[rB]  valE
OPl rA, rB
Write-back
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
Write-back
Write-back
Write-back
Write-back
Write-back
Write back result
R[%esp]  valE
Update stack pointer
R[%esp]  valE
Update stack pointer
int dstE = [
icode in { IRRMOVL, IIRMOVL, IOPL} : rB;
icode in { IPUSHL, IPOPL, ICALL, IRET } : RESP;
1 : RNONE; # Don't need register
];

## Slide 91: Execute Logic
Units
  ALU
    Implements 4 required functions
    Generates condition code values
  CC
    Register with 3 condition code bits
  bcond
    Computes branch flag
Control Logic
  Set CC: Should condition code register be loaded?
  ALU A: Input A to ALU
  ALU B: Input B to ALU
  ALU fun: What function should ALU compute?

## Slide 92: ALU A Input
valE  valB + –4
Decrement stack pointer
No operation
valE  valB + 4
Increment stack pointer
valE  valB + valC
Compute effective address
valE  valB OP valA
Perform ALU operation
OPl rA, rB
Execute
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 4
Increment stack pointer
int aluA = [
icode in { IRRMOVL, IOPL } : valA;
icode in { IIRMOVL, IRMMOVL, IMRMOVL } : valC;
icode in { ICALL, IPUSHL } : -4;
icode in { IRET, IPOPL } : 4;
# Other instructions don't need ALU
];

## Slide 93: ALU Operation
valE  valB + –4
Decrement stack pointer
No operation
valE  valB + 4
Increment stack pointer
valE  valB + valC
Compute effective address
valE  valB OP valA
Perform ALU operation
OPl rA, rB
Execute
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 4
Increment stack pointer
int alufun = [
icode == IOPL : ifun;
1 : ALUADD;
];

## Slide 94: Memory Logic
Memory
  Reads or writes memory word
Control Logic
  Mem. read: should word be read?
  Mem. write: should word be written?
  Mem. addr.: Select address
  Mem. data.: Select data

## Slide 95: Memory Address
OPl rA, rB
Memory
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
No operation
M4[valE]  valA
Memory
Write value to memory
valM  M4[valA]
Memory
Read from stack
M4[valE]  valP
Memory
Write return value on stack
valM  M4[valA]
Memory
Read return address
Memory
No operation
int mem_addr = [
icode in { IRMMOVL, IPUSHL, ICALL, IMRMOVL } : valE;
icode in { IPOPL, IRET } : valA;
# Other instructions don't need address
];

## Slide 96: Memory Read
OPl rA, rB
Memory
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
No operation
M4[valE]  valA
Memory
Write value to memory
valM  M4[valA]
Memory
Read from stack
M4[valE]  valP
Memory
Write return value on stack
valM  M4[valA]
Memory
Read return address
Memory
No operation
bool mem_read = icode in { IMRMOVL, IPOPL, IRET };

## Slide 97: PC Update Logic
New PC
  Select next value of PC

## Slide 98: PC Update
OPl rA, rB
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  Bch ? valC : valP
PC update
Update PC
PC  valC
PC update
Set PC to destination
PC  valM
PC update
Set PC to return address
int new_pc = [
icode == ICALL : valC;
icode == IJXX && Bch : valC;
icode == IRET : valM;
1 : valP;
];

## Slide 99: SEQ Operation
State
  PC register
  Cond. Code register
  Data memory
  Register file
  All updated as clock rises
Combinational Logic
  ALU
  Control logic
  Memory reads
    Instruction memory
    Register file
    Data memory

## Slide 100: SEQ Operation #2
  state set according to second irmovl instruction
  combinational logic starting to react to state changes

## Slide 101: SEQ Operation #3
  state set according to second irmovl instruction
  combinational logic generates results for addl instruction

## Slide 102: SEQ Operation #4
  state set according to addl instruction
  combinational logic starting to react to state changes

## Slide 103: SEQ Operation #5
  state set according to addl instruction
  combinational logic generates results for je instruction

## Slide 104: SEQ Summary
Implementation
  Express every instruction as series of simple steps
  Follow same general flow for each instruction type
  Assemble registers, memories, predesigned combinational blocks
  Connect with control logic
Limitations
  Too slow to be practical
  In one cycle, must propagate through instruction memory, register file, ALU, and data memory
  Would need to run clock very slowly
  Hardware units only active for fraction of clock cycle

## Slide 105: SEQ+ Hardware
  Still sequential implementation
  Reorder PC stage to put at beginning
PC Stage
  Task is to select PC for current instruction
  Based on results computed by previous instruction
Processor State
  PC is no longer stored in register
  But, can determine PC based on other stored information

## Slide 106: Adding Pipeline Registers
W
M
E
D
F

## Slide 107: Pipeline Stages
Fetch
  Select current PC
  Read instruction
  Compute incremented PC
Decode
  Read program registers
Execute
  Operate ALU
Memory
  Read or write data memory
Write Back
  Update register file

## Slide 108: PIPE- Hardware
  Pipeline registers hold intermediate values from instruction execution
Forward (Upward) Paths
  Values passed from one stage to next
  Cannot jump past stages
    e.g., valC passes through decode

## Slide 109: Feedback Paths
Predicted PC
  Guess value of next PC
Branch information
  Jump taken/not-taken
  Fall-through or target address
Return point
  Read from memory
Register updates
  To register file write ports

## Slide 110: Data Dependencies: 1 Nop
0x000:
irmovl
$10,%
edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x006:
irmovl
$3,%
eax
F
D
E
M
W
0x00c:
nop
F
D
E
M
W
F
D
E
M
W
0x00d:
addl
%
edx
,%
eax
F
D
E
M
W
F
D
E
M
W
0x00f: halt
F
D
E
M
W
F
D
E
M
W
# demo-h1.ys
W
R[
%
edx
]
f
10
W
R[
%
edx
]
f
10
D
valA
f
R[
%
edx
]
=
0
valB
f
R[
%
eax
]
=
0
D
valA
f
R[
%
edx
]
=
0
valB
f
R[
%
eax
]
=
0
•
•
•
Cycle 5
Error
M
M_
valE
= 3
M_
dstE
=
%
eax

## Slide 111: Data Dependencies: 2 Nop’s
0x000:
irmovl
$10,%
edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x006:
irmovl
$3,%
eax
F
D
E
M
W
F
D
E
M
W
0x00c:
nop
F
D
E
M
W
F
D
E
M
W
0x00d:
nop
F
D
E
M
W
F
D
E
M
W
0x00e:
addl
%
edx
,%
eax
F
D
E
M
W
F
D
E
M
W
0x010: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-h2.ys
W
R[
%
eax
]
f
3
D
valA
f
R[
%
edx
]
=
10
valB
f
R[
%
eax
]
=
0
•
•
•
W
R[
%
eax
]
f
3
W
R[
%
eax
]
f
3
D
valA
f
R[
%
edx
]
=
10
valB
f
R[
%
eax
]
=
0
D
valA
f
R[
%
edx
]
=
10
valB
f
R[
%
eax
]
=
0
•
•
•
Cycle 6
Error

## Slide 112: Pipeline Summary
Concept
  Break instruction execution into 5 stages
  Run instructions through in pipelined mode
Limitations
  Can’t handle dependencies between instructions when instructions follow too closely
  Data dependencies
    One instruction writes register, later one reads it
  Control dependency
    Instruction sets PC in way that pipeline did not predict correctly
    Mispredicted branch and return
Fixing the Pipeline – see text
  Stalling – CPU sees dependencies & dynamically inserts nops
  Forwarding data directly to next stage(s) rather than wait for the clock

## Slide 113: Pipeline Summary
More modern CPUs use out-of-order execution and parallel execution to achieve faster performance
  Pipelining is still popular in embedded processors